## Slide 1
Fusion Neutronics Meeting 2025
Implicit Stochastic Uncertainty Propagation Scheme for Two-Step Monte Carlo Simulations
I. Lopez, J. Alguacil, J.P. Catalan, P. Sauvan

## Slide 2: Two-Step MC Simulations
Not enough statistical convergence in a single MC simulation.
Events which involve two sequentially coupled particle sources.
First MC Simulation
Intermediate Radiation Source
Second MC Simulation
D

## Slide 3: Stochastic Uncertainty in Two-Step MC Simulations
stochastic uncertainty due to MC1
deterministic calculation
no stochastic uncertainty
stochastic uncertainty due to MC2
stochastic uncertainty in the final nuclear response due to MC1
First MC Simulation
Intermediate Radiation Source
Second MC Simulation

## Slide 4
Fusion Neutronics Meeting 2025
Implicit Stochastic Uncertainty Propagation Scheme

## Slide 5: Random Variable - Requirements
Dependence only on the MC1 radiation field.
Alignment with the stochastic uncertainty in the final nuclear response due to MC1.
applying the
uncertainty propagation law

## Slide 6: Random Variable - Definition

## Slide 7: Random Variable - Requirements
dependence on the MC1 radiation field

## Slide 8: Random Variable - Requirements
applying the
uncertainty propagation law
alignment with the stochastic uncertainty in the final nuclear response due to MC1

## Slide 9: Random Variable - Definition

## Slide 10: Random Variable - Dependence
sensitivity coefficients
constant with respect to the MC1 radiation field
also appear when applying the uncertainty propagation law

## Slide 11: Random Variable - Dependence
particles simulated during MC1

## Slide 12: Random Variable - Assessment
Sensitivity Coefficients
Stochastic Uncertainty MC Simulation
Analogous Neutron MC Simulation
particles simulated during MC1
sensitivity coefficients
First MC Simulation
Intermediate Radiation Source
Second MC Simulation

## Slide 13: Implicit Scheme Advantages
Quantifies the stochastic uncertainty in the final nuclear response due to MC1 as the relative error of the random variable.
MC method capabilities, such as variance reduction techniques and statistical tests.
Eliminates the explicit calculation of the MC1 radiation field covariance matrix.
Avoids any additional assumptions beyond those of the two-step MC simulation method.

## Slide 14: Implicit Scheme Limitations
Estimation of the sensitivity coefficients, no further than previous stochastic uncertainty propagation techniques.
Modifications of MCNP, which undergoes rigorous testing.
Stochastic uncertainty only for a predefined set of tallies.

## Slide 15
Fusion Neutronics Meeting 2025
Implementation in SRC-UNED

## Slide 16: SRC-UNED
Couples two MC simulations using a common geometrical interface, significantly improving the statistical convergence beyond the common geometrical interface, developed within MCUNED+ environment.
J. Catalan, et al., “Development of radiation sources for nuclear analysis beyond ITER bio-shield: SRC-UNED code”, Computer Physics Communications, vol. 275, p. 108309, 2022
particles simulated during MC1
sensitivity coefficients
source contribution to the final nuclear response
WSSA
stochastic uncertainty in the final nuclear response due to MC1
First MC Simulation
Intermediate Radiation Source
Second MC Simulation

## Slide 17: SRC-UNED
J. Catalan, et al., “Development of radiation sources for nuclear analysis beyond ITER bio-shield: SRC-UNED code”, Computer Physics Communications, vol. 275, p. 108309, 2022
Analytical |  |  |  | 
Brute Force |  |  |  | 
Implicit Scheme |  |  |  | 
Analytical |  |  |  | 
Brute Force |  |  |  | 
Implicit Scheme |  |  |  | 

## Slide 18
Fusion Neutronics Meeting 2025
Implementation in R2S-UNED
- JET -

## Slide 19: R2S-UNED
R2S methodology for Shutdown Dose Rate calculations developed within MCUNED+ and ACAB-Loop environments.
P. Sauvan, et al., “Development of the R2SUNED Code System for Shutdown Dose Rate Calculations”, IEEE Transactions on Nuclear Science, vol. 63, nº 1, pp. 375-384, 2016
particles simulated during MC1
sensitivity coefficients
source contribution to the SDR
stochastic uncertainty MC simulation
analogous neutron MC simulation
stochastic uncertainty in SDR due to MC1
Neutron MC Simulation
Neutron Flux
Activation
DGS
Photon MC Simulation
SDR

## Slide 20: R2S-UNED
P. Sauvan, et al., “Development of the R2SUNED Code System for Shutdown Dose Rate Calculations”, IEEE Transactions on Nuclear Science, vol. 63, nº 1, pp. 375-384, 2016
Neutron MC Simulation
Activation

## Slide 21: R2S-UNED
P. Sauvan, et al., “Development of the R2SUNED Code System for Shutdown Dose Rate Calculations”, IEEE Transactions on Nuclear Science, vol. 63, nº 1, pp. 375-384, 2016
Sensitivity Coefficients

## Slide 22: R2S-UNED
P. Sauvan, et al., “Development of the R2SUNED Code System for Shutdown Dose Rate Calculations”, IEEE Transactions on Nuclear Science, vol. 63, nº 1, pp. 375-384, 2016
 | SDR |  |  |  | 
Brute Force |  |  |  |  | 
Implicit Scheme |  |  |  |  | 
 | SDR |  |  |  | 
Brute Force |  |  |  |  | 
Implicit Scheme |  |  |  |  | 

## Slide 23: DTE3 campaign at JET
Photon MC Simulation |  | 
SDR Svh | Relative Stochastic Uncertainty | 
Stochastic Uncertainty MC Simulation (Analogous Neutron MC Simulation) |  | 
Random Variable Svh | Relative Stochastic Uncertainty | Upper Limit
Complete R2S-UNED |  | 
SDR Svh | Relative Stochastic Uncertainty | 
Photon MC Simulation |  | 
 | Relative Stochastic Uncertainty | 
Stochastic Uncertainty MC Simulation (Analogous Neutron MC Simulation) |  | 
 | Relative Stochastic Uncertainty | Upper Limit
Complete R2S-UNED |  | 
 | Relative Stochastic Uncertainty | 
criteria on MC1 reliability
OCT1, DD, IH1, 3H

## Slide 24: Conclusions
Methodology to evaluate overall stochastic uncertainties in two-step MC simulations.
Computational requirements affordable.
Criteria on MC1 reliability.
Future Works
Map of stochastic uncertainties.
Evaluation of systematic uncertainties.

## Slide 25
Fusion Neutronics Meeting 2025
Thanks for your attention,
if you have any questions…?