## Slide 1: GENeuSIS: a novel concept of test bed facility for diagnostics and critical components of ITER
Marta Damiano, R. Villari, P. Gaudio, R. Rossi, & ENEA FNG team
PhD Candidate at Tor Vergata University & ENEA

## Slide 2: Introduction
Diagnostics, electronics and other critical systems installed in ITER will be exposed to complex neutron and gamma radiation fields
Accurate knowledge of the radiation field and its characterization is fundamental to:
  Ensure sufficient protection & demonstrate reliability of diagnostics, electronics and critical systems
  Design and in-situ calibration of neutron diagnostic systems by ensuring the requested accuracy
The radiation field has a large variability in space, energy, angle & time across ITER plasma operations and several responses/effects depends on the energy spectra distribution
The existing neutron facilities are not able to reproduce the complexity and variability of the energy spectra in the locations where the systems are located in ITER
GENeuSIS project

## Slide 3: GENeuSIS project
Assembly to be located in front of DT neutron generator to reproduce in a proper irradiation region the neutron and gamma energy spectra (with embedded gamma sources) expected in the positions in which the components/systems of interest will be installed in ITER.
Neutron diagnostics calibration
Test for critical diagnostics/ systems with low radiation tolerance
Single Event Effects study on electronics
A Novel concept of neutron test bed facility
Recent studies focused to reproduce some ITER relevant neutron energy spectra using the 14 MeV neutrons produced at the Frascati Neutron Generator (FNG).
GENeuSIS
General
Experimental
Neutron
Systems
Irradiation
Station
R. Villari ITPA Diagnostics -43rd ITPA Diagnostics ​May 2023, Eindhoven
Marta Damiano| Fusion Neutronics Meeting Madrid 2025| Page 3

## Slide 4: GENeuSIS Design requirements & features
Modular
Bricks + sheets assemby
Combination of common materials
SS316L, Perpex, Borated polyethilene, Lead, Tungsten, Copper, Teflon, Cd, Boron Carbide, etc...
Trasportable
Easy mounting/dismounting to be used also in other similar neutron facilities.
Flexible
The replacement/substitution of bricks/layers to reproduce various neutron spectra. Housing for gamma sources to reproduce various gamma spectra
Customizable
Experimental cavity (ies) adjustable and customizable to the system/component under test
Multi-purpose
Marta Damiano| Fusion Neutronics Meeting Madrid 2025| Page 4

## Slide 5: ITER Diagnostics EP#12 spectra for GENeuSIS
Location | N flux @ 500 MW (n/cm2/s)
PI-ISS behind Closure plate | 7.62x108
PC#1 | 5.61x105
Emin (MeV) | Emax (MeV) | PI % E | PC % E
1E-11 | 1E-07 | 0.1 | 4.1
1E-07 | 1E-06 | 0.4 | 4.6
1E-06 | 1E-05 | 1.9 | 8.1
1E-05 | 1E-04 | 4.3 | 11.8
1E-04 | 1E-03 | 8.5 | 15.3
1E-03 | 1E-02 | 11.0 | 14.3
1E-02 | 1E-01 | 26.7 | 20.7
1E-01 | 1 | 41.9 | 19.2
1 | 5 | 3.6 | 1.3
5 | 10 | 0.3 | 0.2
10 | 20 | 1.4 | 0.7
PI- behind closure plate
PC #1
PI: diagnostics
PC: electronics
R. Villari Semi-Annual Meeting PrIO SP5, July 2024
Marta Damiano| Fusion Neutronics Meeting Madrid 2025| Page 5

## Slide 6: GENeuSIS design to replicate ITER Port Interspace & Port Cell
GENeuSIS-I
GENeuSIS-II
Port Interspace (GENeuSIS-I)
Port Cell (GENeuSIS-II)
@5x1010 n/s - FNG
R. Villari ITPA Diagnostics -44th ITPA Diagnostics ​Nov 2023, Cadarache
Marta Damiano| Fusion Neutronics Meeting Madrid 2025| Page 6

## Slide 7: Optimization of GENeuSIS-II design
  Reduced dimension, weight & cost
  Enabled the electronics installation & cables connection
Cu
W- Densimet
Pb
SS
Teflon
Air
Perpex
Cd
TEST
AREA
FNG DT target
Assembly 45x80x47 cm3, wt. 1 ton
Emin (MeV) | Emax (MeV) | N flux normalised GENeuSIS/ ITER
1E-11 | 1E-07 | 1.07
1E-07 | 1E-06 | 0.97
1E-06 | 1E-05 | 0.78
1E-05 | 1E-04 | 0.74
1E-04 | 1E-03 | 0.78
1E-03 | 1E-02 | 1.11
1E-02 | 1E-01 | 1.14
1E-01 | 1 | 1.15
1 | 5 | 1.61
5 | 10 | 0.93
10 | 20 | 0.85
Average ratio
1.01 s 0.25
Total Neutron flux in Test cavity: 2.9x10-5 n/cm2/source
5.61x105 n/cm2/s same N flux of ITER Port Cell @ FNG DT intensity ~2x1010 n/s
39 cm
41 cm
Next steps
Engineering design
Procurement of materials
Marta Damiano| Fusion Neutronics Meeting Madrid 2025| Page 7

## Slide 8: GENeuSIS AI: Machine learning development
The simulations made during the design phase of GENeuSIS-I and GENeuSIS-II allowed the generation of a database used for training a supervised machine learning model, based on Neural Networks.
speed up the pre-analysis (from weeks to one day) and select the best combination of materials able to reproduce any further neutron (/gamma) energy spectra.
First step: database generation matrix based instead of string based
Second step: materials fluxes
Third step: Variational AutoEncoder (VAE)
Fourth step: fluxes materials
# | Material
1 | SS
2 | Pb
3 | Perspex
4 | Cd
5 | Cu
6 | Densimet
7 | Teflon
8 | B4C
9 | Air
Marta Damiano| Fusion Neutronics Meeting Madrid 2025| Page 8

## Slide 9
Materials  Fluxes
MATLAB code
Division in training set and test set (90% - 10%)
Initialization of Fully Connected Neural Network [10 5 2 5 10]
Bottleneck technique to avoid overfitting
Ensemble made of 30 Neural Network (NN)
Successfull predictions
GENeuSIS-I AI
GENeuSIS-II AI
GENeuSIS AI: Machine learning development
Marta Damiano| Fusion Neutronics Meeting Madrid 2025| Page 9

## Slide 10: GENeuSIS AI: Machine learning development
VAE: Variational AutoEncoder
It allows the generation of new data similar to the input data
Use an explicit likelihood-based approach, ensuring that the generated data follows a probabilistic model
New fluxes generated with VAE: similar but not equal to the initial ones
If the test points (red) exhibit a significant distance from the training points (blue),
the flux deviates substantially from the reference database
Marta Damiano| Fusion Neutronics Meeting Madrid 2025| Page 10

## Slide 11: GENeuSIS AI: Machine learning development
Fluxes  Materials
Marta Damiano| Fusion Neutronics Meeting Madrid 2025| Page 11
Next steps
GENeuSIS-III: sample spectrum
Targeted MCNP simulations to increase the database
Confusion Matrix: how accurately the model's predictions correspond to the true classifications

## Slide 12
THANK YOU
Marta Damiano| Fusion Neutronics Meeting Madrid 2025| Page 12

## Slide 13: Appendix
Fluxes  Materials
Marta Damiano| Fusion Neutronics Meeting Madrid 2025| Page 13