## Slide 1
Parametric Neutronics Study and Machine Learning-Based Tritium Breeding Ratio Prediction for the ARC Tokamak
*Austin Carter
Ethan Peterson
Alex Creely
James Logan
Matthew Vernacchia
Christoph Hasse
Katie Saltzgiver
Ryanne Kennedy
*acarter@cfs.energy

## Slide 2: Outline
Introduction: What is ARC and how does it breed tritium?
Objectives
OpenMC Methodology: Building the TBR library
Machine Learning Approach
Results & Discussion
  Is the surrogate model accurate for TBR?
  Which parameters have the strongest impact on TBR?
Conclusions
Future Work

## Slide 3: Introduction: What is ARC and How does ARC breed tritium?
CFS is currently constructing SPARC [1]: a compact, high-field tokamak using high-temperature superconductors (HTS)
  Goal: produce fusion gain Q > 2. No contribution to electrical grid
  Major radius: 1.85 m
ARC [2] is a similar tokamak to SPARC, but a demonstration fusion pilot power plant
  ~ 1,000 MW of fusion power
  ARC uses an all-liquid blanket of low pressure, slowly flowing FLiBe molten salt
  Tritium breeding ratio > 1.1
  Major radius: ~4.5 m
1Creely AJ, Greenwald MJ, Ballinger SB, et al. Overview of the SPARC tokamak. Journal of Plasma Physics. 2020;86(5):865860502. doi:10.1017/S0022377820001257
2Sorbom, B. N., et al. ARC: A compact, high-field, fusion nuclear science facility and demonstration power plant with demountable magnets. United States: N. p., 2015. Web. doi:10.1016/j.fusengdes.2015.07.008.
SPARC
ARC

## Slide 4: Objectives
Assess the sensitivity of the tritium breeding ratio (TBR) to key ARC tokamak design parameters
Maintain design flexibility during early-phase ARC development by identifying parameters with the greatest impact on TBR
Use simplified OpenMC simulations to efficiently generate a wide range of ARC design perturbations
Build a comprehensive TBR dataset that spans the relevant multidimensional design space
Train a machine learning surrogate model (TransformerTBRNet) to predict TBR for arbitrary, unseen design points
Ensure the surrogate model operates in a well-populated interpolation regime, avoiding extrapolation

## Slide 5: Methodology
OpenMC Methodology
Machine Learning Methodology
Randomly sample ARC configuration parameters
Build OpenMC model using configuration
Run OpenMC; Tally TBR
Library of TBR values for unique ARC models
Train neural network TransformerTBRNet
Sensitivity studies for determination of most influential design parameters on TBR

## Slide 6: OpenMC Methodology
Perturbed Parameter
Lithium-6 enrichment
Multiplier
Structural Material
Neutron Shield Material
First Wall Thickness
VV Inner Thickness
VVCC Thickness
VV Outer Thickness
Multiplier Thickness (if present)
Port Axial Extent
Port Toroidal Extent
Fraction of FLiBe displaced by structural material
FLiBe Impurity Fraction
Each ARC configuration is defined by a random draw from the sample space of design parameters shown for the definition of a unique tokamak configuration
Sampling was performed uniformly and independently across each parameter’s allowed range
Each configuration is passed to the automated model builder, which generates a fully resolved OpenMC geometry
This approach enables broad coverage of the design space, supporting both sensitivity analysis and surrogate model training
Randomly sample ARC configuration parameters
Build OpenMC model using configuration
Run OpenMC; Tally TBR
Library of TBR values for unique ARC models
Train neural network
Sensitivity studies for determination of most influential design parameters on TBR

## Slide 7: OpenMC Methodology
Leveraged an automated ARC model builder to translate configuration files into fully defined OpenMC [1] models, with lightweight level of detail
Geometry constructed using constructive solid geometry (CSG) with extensive use of openmc.model.Polygon for complex tokamak components
Employed ENDF/B-VIII.0 [2] nuclear data for all neutron interaction cross sections
Tallied tritium production using OpenMC’s built-in "H3-production" score in regions containing FLiBe
Each simulation run used 5 batches of 20,000 histories, balancing accuracy and speed
Achieved an average runtime of ~0.4 CPU-minutes per simulation
The mean 1σ standard deviation on TBR predictions was 0.00328, ensuring high-fidelity data for ML training
1Paul K. Romano, Nicholas E. Horelik, Bryan R. Herman, Adam G. Nelson, Benoit Forget, and Kord Smith, “OpenMC: A State-of-the-Art Monte Carlo Code for Research and Development,” Ann. Nucl. Energy, 82, 90–97 (2015).
2D.A. Brown, M.B. Chadwick, R. Capote, et al., "ENDF/B-VIII.0: The 8th Major Release of the Nuclear Reaction Data Library with CIELO-project Cross Sections, New Standards and Thermal Scattering Data", Nuclear Data Sheets, 148: pp. 1-142 (2018).
OpenMC rendering of an example ARC iteration. Yellow-orange indicates molten salt blanket.
Randomly sample ARC configuration parameters
Build OpenMC model using configuration
Run OpenMC; Tally TBR
Library of TBR values for unique ARC models
Train neural network
Sensitivity studies for determination of most influential design parameters on TBR
R-Z mesh tally for relative distribution of “H3-production”

## Slide 8: Library of TBR values
Normalize TBR to the maximum in the library
Plot shows the entirety of the TBR library categorized by structural material and multiplier material
The enrichment fraction is relative to natural abundance
Randomly sample ARC configuration parameters
Build OpenMC model using configuration
Run OpenMC; Tally TBR
Library of TBR values for unique ARC models
Train neural network
Sensitivity studies for determination of most influential design parameters on TBR
mean 1σ standard deviation on TBR predictions = 0.00328

## Slide 9: TransformerTBRNet
Randomly sample ARC configuration parameters
Build OpenMC model using configuration
Run OpenMC; Tally TBR
Library of TBR values for unique ARC models
Train neural network
Sensitivity studies for determination of most influential design parameters on TBR
1Paszke, A., Gross, S., Massa, F., Lerer, A., Bradbury, J., Chanan, G., ... & Chintala, S. (2019). PyTorch: An imperative style, high-performance deep learning library. Advances in Neural Information Processing Systems, 32, 8024–8035.
Input Features
Size = 21
Parameters of ARC design
Linear Embedding Layer
Projects raw input vector (design parameters) into higher-dimensional space (128)
Add Positional Encoding
Injects positional information (even for non-sequential / tabular inputs)
Transformer Encoder Blocks
2 layers
Multi-head Self-Attention
Feedforward Layer (dim=256)
LayerNorm & Dropout (0.1)
Average Pooling Across Sequence Dimension
Reduces
(batch_size x seq_len x embed_dim) → (batch_size x embed_dim)
Feedforward MLP Head
Linear (128→ 64)
ReLU
Linear (64→1)
Output
TBR Prediction
The TransformerTBRNet architecture was implemented using the PyTorch [1] deep learning framework, enabling efficient model definition, GPU-accelerated training, and flexible experimentation with transformer-based architectures.
Input features include both numerical parameters and one-hot encoded material selections
Data was split into three sets:
  70% Training set: Used to fit model weights
  15% Validation set: Used to monitor generalization performance during training
  15% Test set: Held out entirely until final evaluation
Splitting performed using scikit-learn’s train_test_split with a fixed random seed (random_state=42) to ensure reproducibility
Validation and test sets were drawn separately from the same 30% pool, ensuring the model never sees the test data during training
All sets were normalized using the same scaler, fitted only on the training data, to prevent data leakage

## Slide 10: TransformerTBRNet
Randomly sample ARC configuration parameters
Build OpenMC model using configuration
Run OpenMC; Tally TBR
Library of TBR values for unique ARC models
Train neural network
Sensitivity studies for determination of most influential design parameters on TBR
Loss Criterion: L1 Loss = Mean Absolute Error (MAE)
: true target TBR (OpenMC)
: model prediction (TransformerTBRNet)
: Number of samples in batch (512)
Optimizer: Adam Optimizer
: each parameter at time step
: learning rate = 1E-4
: bias correction
Epoch 998/1000 - Train Loss: 0.0035, Val Loss: 0.0044
Epoch 999/1000 - Train Loss: 0.0035, Val Loss: 0.0042
Epoch 1000/1000 - Train Loss: 0.0035, Val Loss: 0.0040
Ultimately the surrogate model produces L1 loss comparable to OpenMC mean 1σ standard deviation on TBR predictions = 0.00328
Compute Time:
Model trained on a single NVIDIA Tesla T4 GPU
Total training time: 15 minutes (~0.25 GPU-hours)
Estimated compute: ~16.25 TFLOP-hours (mixed precision)
Approx. energy consumption: ~17.5 Wh
Training completed efficiently due to model simplicity and dataset size

## Slide 11: TransformerTBRNet Predictions & Results
Randomly sample ARC configuration parameters
Build OpenMC model using configuration
Run OpenMC; Tally TBR
Library of TBR values for unique ARC models
Train neural network
Sensitivity studies for determination of most influential design parameters on TBR
Varying two parameters that provide significant impact to the TBR
Li-6 enrichment
Structural material choice
Keeping other variables constant
Shielding material = boron carbide
No multiplier
Nominal port size
Nominal VV dimensions

## Slide 12: TransformerTBRNet Predictions & Results
Randomly sample ARC configuration parameters
Build OpenMC model using configuration
Run OpenMC; Tally TBR
Library of TBR values for unique ARC models
Train neural network
Sensitivity studies for determination of most influential design parameters on TBR
Varying two parameters that provide significant impact to the TBR
Li-6 enrichment
Multiplier layer embedded in the Vacuum vessel cooling channels
  Hence the cooling channels’ volume is reduced with more multiplier
Keeping other variables constant
Shielding material = boron carbide
Vanadium alloy structural material
Nominal port size
Nominal VV dimensions, slightly enlarged cooling channel volume

## Slide 13: TransformerTBRNet Predictions & Results
Randomly sample ARC configuration parameters
Build OpenMC model using configuration
Run OpenMC; Tally TBR
Library of TBR values for unique ARC models
Train neural network
Sensitivity studies for determination of most influential design parameters on TBR
Varying parameters individually, normalize from max to min of each
Keeping other variables constant
Use a beryllium multiplier in the cooling channel
Sensitivity coefficients on next slide
It is clear how much more impactful Li-6 enrichment is relative to other design parameters

## Slide 14: TransformerTBRNet Predictions & Results
Randomly sample ARC configuration parameters
Build OpenMC model using configuration
Run OpenMC; Tally TBR
Library of TBR values for unique ARC models
Train neural network
Sensitivity studies for determination of most influential design parameters on TBR

## Slide 15: Conclusions
✅ Successfully generated a large, high-quality dataset of TBR values using a streamlined OpenMC modeling framework with automated ARC geometry perturbations
✅ Developed and trained a neural network surrogate model (TransformerTBRNet) capable of predicting TBR values across a multidimensional design space with high accuracy
🔍 Used the surrogate to systematically evaluate TBR sensitivity coefficients, quantifying the relative impact of various design parameters
🧱 Demonstrated a structured approach to assess the influence of material selections and geometric features on TBR response
➕ Enabled the efficient exploration of design tradeoffs by varying model parameters and observing predicted responses in TBR
🧪 Confirmed the capability of using automated neutronics pipelines to handle statistically meaningful variation across complex tokamak components
🧭 Verified that the surrogate model operates within a well-interpolated region of the design space, supporting reliable predictions without extrapolation risk

## Slide 16: Future Work
🌡️ Incorporate realistic temperature profiles in the FLiBe blanket model to capture temperature-dependent neutron cross sections and fluid behavior
📐 Study the impact of geometry of both the vacuum vessel and blanket, including shaping and segmentation, on neutron streaming and breeding efficiency
🧱 Evaluate alternative blanket and shield geometries, particularly reshaping or re-optimizing the inboard neutron shield to balance tritium breeding and magnet protection
🧪 Include more detailed isotopic and chemical effects, including usable tritium molecular formation and transport behavior
🔁 Model time-dependent effects on TBR, such as burnup, irradiation damage, and material evolution over ARC lifetime
🧠 Improve surrogate model interpretability with tools like SHAP and uncertainty quantification
🚀 Use the surrogate model in automated design optimization to identify TBR-compliant ARC configurations with minimal cost or material burden

## Slide 17
Questions?
*acarter@cfs.energy