## Slide 1
Extended Adjoint Driven Importance Solution (XADIS)
Presented by: Andrea Saltos (CFS)
Contributors: Michael Saitta (MPR), Eugene Sosnovsky (CFS), Ryanne Kennedy (CFS)

## Slide 2: Commonwealth Fusion Systems
At Commonwealth Fusion Systems (CFS), we are developing the SPARC fusion device:
  High magnetic field, compact tokamak designed to achieve net energy gain
  Employs advanced high-temperature superconducting (HTS)
  Goal is to achieve Q >1
  Fusion power of ≈ 140 MW
SPARC

## Slide 3: Neutron Diagnostics
Neutron diagnostics systems is the main tool to calculate fusion power
Design of neutron diagnostics relies on radiation transport simulations
  Optimization of geometry
  Selection of materials
  Estimate detection efficiency
  Prediction of interference in detector responses
E.g., due to scattered neutrons from different components of the tokamak as well as structural materials

## Slide 4: Scattering contribution
Question we need to answer:
What is the scattering contribution from different regions in the tokamak hall to a detector response?
The importance of scattered neutrons to a detector could be calculated using standard Monte Carlo(MC) simulations
  Slow convergence and limitations of available MC codes, make quick design iterations and parametric studies difficult.
We have developed a framework that uses deterministic transport and contiguous unstructured mesh models
  Minimizes computational effort
  Enables fast scoping analyses to inform detector design and prioritization of hardware installation
Detector
Ref: Raj et al., Rev. Sci. Instrum. 95, 103507 (2024)

## Slide 5: Neutron transport theory
Recall the transport equation:
= angular unit vector
= total cross section
= particle flux
= dependence on space, energy and angle
= scatter cross section
= source
spatial variation
material interaction
scatter
flux
source

## Slide 6: Detector response
= forward flux
= response function
= space, energy, and angular coordinates of the particle
The detector response is given by:
We can rewrite this as:

## Slide 7: Adjoints
The "importance" of particles throughout the system that contribute to the response corresponds to the adjoint flux, for this detector.
The importance function and the flux are interconnected by
material interaction
scattering
Adjoint flux
Adjoint source
spatial variation
Notes: Obeys the adjoint Boltzmann equation with a source equal to the detector response, 𝑄^†.
The detector response is related to the adjoint by

## Slide 8: Contributon theory
If we multiply the forward and the adjoint transport equation by and , respectively, and then we subtract we get
In-scattering
out-scattering
Contributon transport equation : describes the simultaneous transfer of response through space and energy.
Ref: Williams, M. L. Nuc. Sci. and Eng. 108.4 (1991): 355-383.
Notes: -

## Slide 9: Scattering contributon
What is the fractional contribution of particles that are born at a certain point?
(scattering source)
contribution at a point in space
contribution over entire domain
Or:

## Slide 10: Implementation
The Attila determinsitic solver gives us what we need:
adjoint solution
cross sections
forward solution
We can compute the integrals using spherical harmonics:

## Slide 11: Sample case 1: double slab
Two blocks of material: 1) alumina and 2) water
DD fusion source
Neutron flux “detector” target
Coarse discretization for testing
Scattering contribution:
  Material 1: 65 %
  Material 2: 35%
forward
adjoint
Fractional contribution
material 1
material 2
source
detector

## Slide 12: Sample Case 2: blocks in a room
Two blocks of material: 1) water and 2) alumina
DD fusion source
Neutron flux “detector” target
Coarse discretization for testing
forward
adjoint
contribution
source
detector
material 1
material 2
Scattering contribution:
  Material 1: 40.7%
  Material 2: 59.1 %

## Slide 13: Verification
MCNP comparison to verify our tool
Question:
  What portion of particles that score in the target region have experienced a scattering event in region X?
Answer:
  Run PTRAC and filter particles by those that score in the target.
  Parse the history for each of them and count how many had scattering events in each region.

## Slide 14: XADIS: Attila vs MCNP (contribution from material 2)
Geometry | Material 1 | Material 2 | Source Spectra | XADIS | MCNP | Difference
Double Slab | SS316 | Water | DT | 52% | 50% | 4%
Double Slab | SS316 | Water | DD | 30% | 26% | 12%
Double Slab | SS316 | Water | 100 keV | 11% | 10% | 15%
Double Slab | Be/Cu | Al-6061 | DT | 35% | 30% | 17%
Double Slab | Be/Cu | Al-6061 | DD | 42% | 41% | 3%
Double Slab | Be/Cu | Al-6061 | 100 keV | 44% | 37% | 21%
Double Slab | Steel | Copper | DT | 53% | 61% | -13%
Double Slab | Steel | Copper | DD | 50% | 58% | -14%
Double Slab | Steel | Copper | 100 keV | 38% | 45% | -16%
Double Slab | FLiBe | Water | DT | 53% | 51% | 4%
Double Slab | FLiBe | Water | DD | 33% | 30% | 9%
Double Slab | FLiBe | Water | 100 keV | 20% | 20% | 3%
Double Slab | Alumina | Water | DT | 52% | 51% | 1%
Double Slab | Alumina | Water | DD | 35% | 33% | 4%
Double Slab | Alumina | Water | 100 keV | 33% | 30% | 10%

## Slide 15: Conclusions
We have developed a framework that uses deterministic transport to determine the scattering contribution to a detector response
  Based on contributon theory
  Evaluates the related mathematical operations on spherical harmonic moments using the macroscopic multigroup cross sections, and the adjoint and forward flux.
  Implemented for use with the Attila deterministic Solver
  Informs what regions/physics are important in different parts of the tokamak or tokamak building (needed for detector design and placement of equipment)
  Minimizes computational effort

## Slide 16: Future work
Conversion to C++ for improved run times
Optimization of the visualization tool
Further testing
Look at other physics
  Reactions
  Specific Isotopes

## Slide 17: Acknowledgements
The Nuclear Engineering Team at
In partnership with

## Slide 18: MCNP Verification
Cell 3
Just use PTRAC!
For each particle that scores
  Every time that it has a collision event
    Track what that histories eventual contribution to the tally is
Sum the contributions to the tally for each history for each cell
Provides a scatting contribution.
Cell 2
Cell 1
(Source)
Cell 4
(Detector)
track length contribution
collision
collision