## Slide 1
Neutron shielding of low aspect ratio torii modeled by Monte Carlo methods and Machine Learning
Brice Alan OTT – Renaissance Fusion – alan.ott@renfusion.eu
Victor PROST – Renaissance Fusion – victor.prost@renfusion.eu
Francesco A. VOLPE – Renaissance Fusion – francesco.volpe@renfusion.eu
Elliot ENGLISH – Renaissance Fusion – Elliot.English@renfusion.eu

## Slide 2
Liquid metal port
Deuterium – tritium plasma
Cryostat
Reactor blanket
Liquid metal + shielding
HTS magnet and structure
Overall Aim of Renaissance Fusion:
Build a compact stellarator with Liquid Metal first wall
Major radius | On axis field | Aspect ratio | Plasma volume | Reactor Power
3.8 m | 10.2 T | 4.1 | 65 m3 | e
3.8 m | 10.2 T | 4.1 | 65 m3 | 
liquid metal (Pb + Li-LiH) neutronic shielding (TiH2, VH2)
Fama, F. et al. – 2022 - An optimized power conversion system for a stellarator-based nuclear fusion power plant
Prost, V., Volpe, F. A. - 2024 - Economically optimized design point of high-field stellarator power-plant
Prost, V., Ogier-Collin, S., Volpe, F. A. - 2024 - Compact fusion blanket using plasma facing liquid Li-LiH walls and Pb pebbles
Blanket functions :
1. Heat removal
Extract heat from the plasma and transfer to the power conversion system
2. Tritium breeding
Produce tritium to fuel the fusion reaction – tritium breeding ratio (TBR)
3. Radiation shielding
Protect structures, coils, and environment from radiation damages

## Slide 3
1D neutronic model provided initial results but relied on simplistic cylindrical geometry
* Prost, V., Ogier-Collin, S., Volpe, F. A. - 2024 - Compact fusion blanket using plasma facing liquid Li-LiH walls and Pb pebbles
Functions and requirements | Targets | Designed
Heat removal | - | > 92 % nuclear heat on LM layers
Energy multiplication |  | 
Tritium breeding ratio |  | 
Total fluence on HTS coils | < | 
LM vessel DPA | < 200 DPA | ~100 DPA
Magnet structure DPA | < 200 DPA | < 1 DPA
Functions and requirements | Targets | Designed
Heat removal | - | > 92 % nuclear heat on LM layers
Energy multiplication |  | 
Tritium breeding ratio |  | 
Total fluence on HTS coils |  | 
LM vessel DPA | < 200 DPA | ~100 DPA
Magnet structure DPA | < 200 DPA | < 1 DPA
Neutron shielding
Heat extraction
Primary confinement vessel
OpenMC - ENDF/B-VII.1
R = 3.8m
a = 0.9m
A = 4.1
91cm
Limitations:
- Parametric manual search/optimization (long) - 1D geometry is an initial guess but we need a more robust and generalizable tool
40 years with 80% availability

## Slide 4
Developed a torus shape neutronic module to be included in stellarator systems code
Neutronic model
Performance:
Accurate evaluation of the material configuration
Fast evaluation of the reactor performance
FIXED
CONSTRAINED TARGET PERFORMANCE
THICKNESS TO MINIMIZE
Input:
Reactor major radius
Reactor minor radius
Fusion power
Blanket material thicknesses
Output:
Tritium breeding ratio
Energy multiplication
Power deposited in LM layer
Neutron flux
Radiation damage
Neutronic module in the System Analysis
Solution:
Surrogate model for the high-fidelity neutronic model
Optimization loop

## Slide 5
Reduced ML model optimisation scheme
5
Neutronic simulations (~10-30mins)
Reduced ML model (~ms)
Genetic algorithm optimization
Parametric Torus
Plasma
Low aspect ratio stellarators
Plasma
Spherical tokamaks
Parametric D-shaped torus
Verification with High fidelity code

## Slide 6: Input data for ML – generation of 20 000 configurations
  Generation:
  Tallies output with tagged UUID result file
  Decrease 1 run time from days => tens of minutes => few minutes
  About 2 full weeks to generate the input data for ML
min, max, discretization
Reduced angle: 18°
*https://inis.iaea.org/records/231pm-zzy35
Surface reflection
Surface reflection
- Reduced angle: profiting of the symmetries with
- Variance Reduction with Pre-build feature MAGIC*
Parameters | Min | Max | Discretisation
Reactor [cm] |  |  | 
Minor Radius | 50 | 200 | 10
Major Radius | 300 | 600 | 10
Eccentricity | 0 | 15 | 0.5
Blanket [cm] |  |  | 
Lead | 1 | 20 | 0.5
LiLih | 5 | 45 | 0.5
SiC | 5 | 5 | 0.5
VH2 | 10 | 60 | 0.5
Steel (Boronated) | 10 | 10 | 0.5
REBCO baffers | 0.0441 | 0.0441 | 0.0441
Steel (Boronated) | 40 | 40 | 0.5
Parameters variations:
Acceleration of the simulations
VARIED
VARIED
VARIED

## Slide 7: ML model accurately predicts neutronic simulations
Configuration data :
R | r | ecc |layers ( material, thickness)
Formalized in a 700 elements vector for layer configuration (discretization at 0.5 cm) with material coding
Train and Test sets: 80%, 20%
Training time: 30 minutes with 16 cpus
Comparison with “Reference case”:
The uncertainties are under control regarding the constraints' precision and model accuracy
Quantity | Diff {Pfus=1.8GW, R=3.8m, r=0.9m}
TBR | 4.4%
Energy Mult | 0.9%
Energy removal [%] | 0.7%
Fluence on Coil [cm2/n] | 26.8%
DPA on coil [dpa/n] | 30.9%
DPA on Liquid metal [dpa/n] | 46.0%
Pb, 2cm
LiLih, 3cm
SiC, 1cm
1
1
1
1
2
2
2
2
2
2
3
3
3
Geom
 | Optimization : Adam at learning rate 2E-3 |  |  |  | 
layer | Activation | Constraints | Units | Batch Normalization | Dropout (Rate)
Input | - | - | 703 | - | -
Dense | ReLU | L1, L2 | 256 | Yes | 0.3
Dense | ReLU | L1, L2 | 128 | Yes | 0.3
Dense | ReLU | L1, L2 | 64 | Yes | 0.3
Dense | ReLU | L1, L2 | 32 | Yes | 0.3
Output | ReLU | L1, L2 | 6 | - | -
Results data :
TBR | Energy mult | Heat removal| Fluence on coils | DPA on coils structure| DPA LM vessel
Machine learning Model:
Notes: Adam optimization at learning rate 2E-3
Drop out : prevent Overfitting
Regularization L1/L2 => Overfitting
Batch Normalisation : Stabilize and accelerate the training
MSE (Mean Squared Error )
MAE (Mean Absolute Error)

## Slide 8: Genetic Algorithm for a minimal blanket – Get results in 15 min
Set the input reactor parameter for a minimal blanket
min, max, discretization
Performance:
About 15 minutes per 16 CPUs.
Verification
High Fidelity code
Reactor parameter |  |  | 
Pfusion, Major radius, Minor radius, Eccentricity |  |  | 
Blanket [cm] |  |  | 
Parameters | Min | Max | Discretisation
Lead | 1 | 20 | 0.5
LiLih | 5 | 45 | 0.5
SiC | 5 | 5 | 0.5
VH2 | 10 | 60 | 0.5
Steel (Boronated) | 10 | 10 | 0.5
REBCO baffers | 0.0441 | 0.0441 | 0.0441
Steel (Boronated) | 40 | 40 | 0.5
Category | Parameters
Genetic Algorithm | Population Size: 2000, Generations: 15, …
Optimization Weights | TBR: 1.0, Energy Multiplication: 1.0, Heat Removal: 1.0, Fluence HTS: 1.0, DPA HTS: 1.0, Thickness: 1.0
Target Values | TBR: 1.15, Energy Multiplication: 1.0, Heat Removal: 95.0, Fluence HTS: 1.0e+19, DPA LMS: 200.0, DPA HTS: 200.0
Additional Parameters | Thickness Penalty Weight: 1.0, Adaptive Penalty: Min Weight: 0.1, Max Weight: 1000.0
* A weighted – fair allocation , Mo and Walrand 2000
Set the input Genetic Algorithm parameters
Implementation : α-Fair allocation* principle
Suppose chosen to
Maximise
Subject to
Tlead=1/2 TLiLIH

## Slide 9: Surrogate models for 3D stellarator and tokamak predict neutronic simulations within tens of percent
min, max, discretization
Quantity | 3D High Fidelity | 3D Surrogate | Differences
TBR | 1.52 | 1.66 | -8.4%
Energy Multiplication | 1.21 | 1.19 | 1.4%
Heat Removal | 93.7 | 95.2 | -1.7%
Fluence HTS (cm²/s/n) | 7.20E-11 | 1.18E-10 | -39.2%
DPA HTS (dpa/n) | 1.55E-32 | 2.44E-32 | -36.6%
DPA LM (dpa/n) | 2.22E-28 | 2.52E-28 | -12.2%
Plasma
Added shielding
Plasma
Parametric Torus with eccentricity
Low aspect ratio stellarators
Spherical tokamaks
Parametric D-shaped torus*
Quantity | 3D High Fidelity | 3D Surrogate | Differences
TBR | 1.64 | 1.66 | 1.5%
Energy multiplication | 1.20 | 1.20 | 0.2%
Heat removal | 94.5 | 96.7 | 2.4%
Fluence HTS [cm2/n] | 4.73E-11 | 5.31E-11 | 12.2%
DPA HTS [DPA/n] | 1.65E-32 | 2.27E-32 | 37.6%
DPA LM [DPA/n] | 5.09E-28 | 2.13E-28 | -58.1%
9
*Preliminary investigation of neutron shielding compounds for ARC-class tokamaks Fusion Engineering and Design 185 (2022) 113335

## Slide 10: Optimization Module align with the Reference case
min, max, discretization
Plasma
Parametric Torus with eccentricity
Low aspect ratio stellarators
Thickness [cm] | Reference* | 3D Surrogate | Status
Lead | 10 | 11 | Optimized
LiLih | 22 | 22 | Optimized
SiC | 5 | 5 | Fixed
VH2 | 54 | 53 | Optimized
Steel | 10 | 10 | Fixed
HTS | 0.04 | 0.04 | Fixed
Total | 101 | 101 | 
*Compact fusion blanket using plasma facing liquid Li-LiH walls and Pb pebbles Journal of Nuclear Materials 599(3):155239

## Slide 11
Reduced ML model optimization scheme highlights benefits for high power reactors (1 GWe vs 100 MWe)
11
Neutronic simulations (~1-30mins)
Reduced ML model (~ms)
Genetic algorithm optimization
Low aspect ratio stellarators
0.5 | 1.0 | 1.5 | 2.0 | 2.5 | 3.0
Fusion Power [GW]
Radial build [cm]
120
100
80
60
40
20
0
X2 in fusion power  ~5/6 cm increase thickness

## Slide 12
120
100
80
60
40
20
0
Model optimization scheme shows limited impact of reactor’s aspect ratio
12
Neutron flux scales with ~ A-1/3
With constant volume (100 m3 ) and power (2 GW)
Radial build [cm]
1.8 | 2.9 | 4.3 | 5.7 | 7.4 | 9.2 | 11.0 | 13.0 | 15.2 | 17.4
Aspect ratio [-]
Radial build [cm]

## Slide 13
Take aways
Machine learning model developed for rapid neutronics performance prediction
Genetic algorithm used to optimize blanket configuration
Key findings:
  Efficient optimization of blanket thickness and composition
  Slight increase in blanket thickness needed for higher fusion power
  Limited impact of reactor aspect ratio on neutronics performance
Methodology enables rapid, optimized design for compact fusion reactors
Studies (scan over aspect ratio and run power) within hours range instead of multiple days with manual search
Potential for extension to other reactor design aspects