## Slide 1
F4Enix
A new Python API for pre and post processing of MCNP inputs and outputs
Alberto Bittesnich*, Davide Laghi, Alvaro Cubi, Aljaz Kolsek, Marco Fabbri
08/04/2025

## Slide 2: Outline
Introduction:
  Code development at F4E
  F4Enix structure and available resources
  Important dependencies
F4Enix API
  MCNP input
  D1S-UNED
  Mctal
  MCNP output
  Meshtal
  Other…
Conclusion

## Slide 3
Introduction

## Slide 4: F4E neutronics tools
An extensive set of neutronics tools have been developed at F4E or under F4E auspices during the last years.
Focused on automatic pre- and post-processing of MCNP input and outputs to increase efficiency and capability. But also nuclear data V&V (JADE), or nuclear waste classification (F4E-Radwaste)
Available on GitHub organization page (https://github.com/Fusion4Energy).
We strongly believe in the open-source development as driver for upstream improvements and to avoid duplication of tasks.

## Slide 5: F4E neutronics tool
RadModeling
mesh2vtk
vtkconverter
rssa_analyzer
mctools
DoseMap-calculator
iMCNP_Source
JADE
F4Enix
atlas
Independent tools
Maintained, tested and documented in a single place
Easy installation (pip) and integration with other python tools
F4E-Radwaste
https://github.com/Fusion4Energy
iWW_GVR

## Slide 6: Installation and resources
Code hosted open-source on GitHub:
https://github.com/Fusion4Energy/F4Enix
Continuous Integration for Windows and Linux, python from 3.9 to 3.11
Online html searchable documentation:
https://f4enix.readthedocs.io/en/latest
F4Enix documentation features:
A brief introductory tutorial on how to use the API
A series of jupyter notebooks examples
Complete F4Enix API
Installation instructions
Link to Github repository
…
pip install f4enix

## Slide 7: Important dependencies
Numjuggler
https://pypi.org/project/numjuggler/
The MCNP input parser of F4Enix is built on top of the numjuggler parser. This guarantees easier usage and additional features. Nevertheless, all input cells, surfaces and data cards are still stored as numjuggler objects
F4Enix has many dependencies from other python packages, but three of them are particularly important for the users. Knowledge of how to use these packages is not strictly needed but can significantly improve the user experience

## Slide 8: Important dependencies
pandas
https://pandas.pydata.org/
Tally results and any kind of tables or summary are always provided as pandas DataFrame objects that can be easily dumped to .csv or excel format.
pandas provides a number of very useful tools to manipulate data that can be extremely useful when building a post-processing pipeline

## Slide 9: Important dependencies
PyVista
https://docs.pyvista.org/version/stable/index.html
FMESH results are ultimately provided as pyvista grids

## Slide 10
F4Enix API

## Slide 11: F4Enix API scheme Overview
f4enix
input
output
MCNPinput
D1S_input
d1suned
Input
IrradiationFile
ReactionFile
eeout
mctal
meshtal
rssa
MCNPoutput
ww
EEOUT
Mctal
Fmesh
Meshtal
RSSA
Output
module
class
*only main modules and classes are reported here
WW
Elite_input
ace
F4Enix API is thought to be used mainly within a jupyter notebook or via interaction with Python interpreter
Interaction via scripting is also viable
!! --> Training by Alberto Bittesnich & Davide Laghi on Day 4, 11.30-13:00 !!

## Slide 12: Working with MCNP input files
Overview
F4Enix MCNP input API:
Read/write input files
Cell modification: material, density, fill, universe, importance…
Addition of surfaces to cells definition, cells union, cells hashing…
Surfaces parsing and modification
Parsing of materials
From atom to mass fraction
Generation of new materials and materials mixtures
Translation between libraries
Cells/Universes extraction
Sectors’ extraction from E-Lite
Inputs merging
F4/F6 tallies definition
…

## Slide 13: Working with D1S-UNED files
D1S_input
It is possible to generate all possible reactions that could originate from the materials contained in the MCNP input
A D1S_input may also include its radiation and irradiation file
Or given an irradiation file (i.e., all important daughters have been defined), the reaction file can be automatically generated.

## Slide 14: Working with D1S-UNED files
Reaction and Irradiation files
Simple files structures that are fully parsed.
Everything on this files is organized in single Reaction and Irradiation objects.

## Slide 15: Working with E-lite model
Extraction of sectors from E-lite 360 degrees model

## Slide 16: Working with acefiles and microscopic cross-sections collapsing
Several standard energy groups are predefined
Microscopic cross-sections can be retrieved as continuous functions of energy and then collapsed into groups --> useful for reaction rates calculations!

## Slide 17: Working with MCTAL file
Mctal file results are organized in pandas dataframes, useful for data analysis!

## Slide 18: Working with MCNP output files
Debug for lost particles
Vtk (.vtp)
.csv
.xlsx
Readable on ANSYS SpaceClaim with RadModeling!

## Slide 19: Working with MCNP output files
Statistical checks and other tables
Global information
Single tally

## Slide 20: Working with meshtal files
Parsing and dumping
++ Cell-under-Voxel meshes can be parsed and cell filtering can be made
++ parsing MESHINFO Cell-under-Voxel files

## Slide 21: Working with meshtal files: MeshPlotter class
Automatic slicer
Useful methods are provided to do automatically slicing of the mesh results that can be later used for the build of plot atlases.

## Slide 22: Working with meshtal files: Atlas class
Plot and build the atlas
Quite a few parameters have been exposed so far from the
PyVista plotter to control different aspects of the plots

## Slide 23: Example of atlas: mode 0 in-vessel radiation maps
With a bit more code …

## Slide 24: Working with eeout files (Unstructured Meshes)
Get a PyVista grid from the parsing of .eeout file. (limited to 1st and 2nd order tetra for the moment)

## Slide 25: Working with weight windows files
GVR Weight Windows WWINP can be automatically generated from a MESHTAL file…
… and then modified, plotted or exported to VTK

## Slide 26: Working with RSSA files
Complete parser for the RSSA (surface sources) is also included in F4Enix

## Slide 27
Conclusion

## Slide 28: Conclusion
F4E neutronics team has developed a significant number of tools related to neutronic simulations during the years and they all have been released as open-source on GitHub in order to share knowledge with the fusion community
The capabilities of the tools have been entirely included in F4Enix
The purpose of the development of F4Enix is to increase efficiency of analyses workflow and to minimize human errors, while focusing on physics and results interpretation
Have a unique python API for the parsing and manipulation of input and output files provides a number of benefits:
  Maintenance in a single place
  Easier installation (pip)
  Centralization and improvement of documentation
  Continuous Integration (testing, docs, pip)
  Better integration both internally and externally (e.g. lost particle debug)
  F4Enix is open-source, both suppliers and DAs contributions to the development are welcome

## Slide 29
Thank you for your attention!
Follow us on:
www.f4e.europa.eu
www.twitter.com/fusionforenergy
www.youtube.com/fusionforenergy
www.linkedin.com/company/fusion-for-energy www.flickr.com/photos/fusionforenergy