## Slide 1
F4Epurity: A tool for rapidly assessing the change in dose rate resulting from deviations in material impurity content
Alex Valentine1, Tim Eade1, Marco Fabbri2, Matteo di Giacomo3, Davide Laghi2, Raul Pampin2
1UK Atomic Energy Authority, Culham Campus, Abingdon, OX14 3DB, 2Fusion for Energy, Josep Pla 2, Barcelona 08019, Spain, 3ATG Science & Engineering SL, Plaza de Ernest Lluch y Martín 5, Barcelona 08019, Spain
Fusion Neutronics Meeting 2025, Madrid, Spain

## Slide 2: Contents
Introduction and motivation
Theory and implementation
  Maps of effective cross section and activity
  Maps of global and local dose deviations
  Additional code capabilities
Tool validation and future work
Summary

## Slide 3: Introduction and motivation

## Slide 4: Impurity requirements at ITER
The shutdown dose rate resulting from the activation of components depends directly on the chemical composition of materials, not only alloying elements but also, and in many cases more significantly, their impurity content.
ITER has specific project requirements related to the impurities in chemical compositions that must be adhered to.
As ITER construction progresses, deviations and non-conformities are arising in relation to these requirements.
  COTS & standard parts made of uncertified batches
  Unavailability of testing
2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
3 | 3 | 10 | 10 | 5 | 12 | 45
ITER Deviation Requests related to material impurities

## Slide 5: Impurity requirements at ITER
Assessing the impact of each of these deviations by rigorous Monte-Carlo calculation is not practical.
Risk is that safety demonstration does not keep up with the ITER baseline.
Generally engineering judgement or prior experience needed/ approximation based on minimal activation calculation.
Rationalisation needed also in the context of ongoing nuclear rebaselining at ITER.
Develop a tool capable of providing a rapid assessment of the local impact of a given impurity deviation on the shutdown dose rate
Juarez et al., ITER full model in MCNP for radiation safety demonstration, Nature Communications volume 15, Article number: 8563 (2024)
For further details, please see M.Fabbri/R.Pampin talk from day 1

## Slide 6: F4Epurity
Originally developed by UKAEA under F4E framework contract OMF-0882-02-01. Further developed by F4E and UKAEA in a joint collaboration.
Tool is open source and maintained on GitHub: https://github.com/Fusion4Energy/F4Epurity with documentation hosted here: https://f4epurity.readthedocs.io/en/stable/. CI testing pipeline.
Written in Python as a command line tool.

## Slide 7: Theory and implementation

## Slide 8: Reaction Rate calculation
Reaction rate is calculated using an effective cross section. Outside the bioshield, the radiation maps for ITER are available in 5 energy groups*.
5 group cross sections produced for important elements using the pointwise TENDL 2017 data. Includes metastable pathways.
* Note that provided the xs is available to the code, any group format can be used.

## Slide 9: Effective cross section maps
Co59(n,g) Co60
Co59(n,g) Co60
f4epurity-xs --element Co --input_flux ./flux_spectrum.vtr
3D maps of the collapsed cross section are output in VTR format.
Cross sections prepared for cobalt, niobium and tantalum as the dominant drivers of SDDR.
Effective cross section plots output for all reaction pathways for the specified element.
Notes: Note that we have generalized the tool to accept any element as input. Co, Nb and Ta are ITER specific.

## Slide 10: Activity and dose calculation
The activity is calculated from the reaction rate with an ‘activation function’.
All reaction channels are accounted for including to metastable states and decay chains are evaluated to a stable daughter product to determine the activity at the decay time of interest.
The dose is determined used pre-computed conversion factor available for all nuclides. These are provided for each nuclide in units of:
The dose at some distance is then calculated analytically. For a point source, this is a simple 1/r2 relation. For a line source this is given by:

## Slide 11: Activity and dose calculation
The activity is calculated from the reaction rate with an ‘activation function’.
All reaction channels are accounted for included to metastable states and decay chains are evaluated to a stable daughter product to determine the activity at the decay time of interest.
The dose is determined used pre-computed conversion factor available for all nuclides. These are provided for each nuclide in units of:
The dose at some distance is then calculated analytically. For a point source, this is a simple 1/r2 relation. For a line source this is given by:
Notes: Distribution and quantitative result compare well.

## Slide 12: Activity maps
f4epurity-activity --element Co --delta_impurity 0.05 --input_flux ./flux_spectrum.vtr --irrad_scenario SA2 --decay_time 1e6
Co
Bq/g
Co
Bq/g
3D maps of the computed activity are output in VTR format.
Requires input of the irradiation scenario and the decay time of interest to output the activity.
Notes: ~1.2 million voxels in which the calculation is performed across each reaction channel. Highlight NB cell region

## Slide 13: Deviation in dose rate
element: Co
delta_impurity: 0.05
input_flux: radmap_path
irrad_scenario: SA2
x1: [-835]
y1: [1994]
z1: [1230]
x2: [100]
y2: [2019]
z2: [1230]
decay_time: 1e6
The maps for the deviation in dose are output in VTR format or viewed using in-built plotter.
Currently supported source geometries are point or line.
Multiple source terms accepted e.g. deviation in multiple TCWS valves. Individual and summed dose maps are output.
As the number of input arguments is large, they can be defined in a separate json or yaml file.
f4epurity --cfg config.yaml –-sources_csv source.csv
Example yaml file for a line source

## Slide 14: Additional capabilities and future work
Output tabulated dose rates can be extracted at workstation locations (provided as coordinates).
Estimate the impact of shielding on the dose rate for a given source term using buildup factors and attenuation coefficients.
The major limitation of the default maps output by the tool is the assumption of unshielded and unscattered conditions.
  An MCNP SDEF can be written by the tool using the activities output from F4Epurity.
  We have explored the use of an adjoint flux calculation to map contributions to locations of interest.
Complete list of capabilities of the tool is given in the documentation: https://f4epurity.readthedocs.io/en/stable/

## Slide 15: Validation

## Slide 16: Comparison to FISPACT-II
Number of nuclides calculated compared to FISPACT by irradiating 1kg of Co and Nb for DT1 and comparing at 106 seconds.
Comparison performed against code equivalent time correction factors and those used in D1SUNED.
Agreement is found to be very good (within 1%).
Isotope | D1S Time correction factor | Tool derived time correction factors using D1S irradiation schedule
Co60 | 3.686E-02 | 3.685E-02
Nb94 | 1.853E-05 | 1.853E-05
Nb92m | 8.514E-02 | 8.511E-02

## Slide 17: Summary
A novel open source tool, F4Epurity, has been developed to rapidly assess the change in dose rate resulting from deviations in material impurity content.
The estimation provided can be determined in minutes vs rigorous 3D Monte-Carlo calculation (days).
The code has been designed to be flexible for application not only to ITER.
The tool will be useful in managing the growing number of non-conformances at ITER and as part of rationalisation for ITER impurity requirement throughout the tokamak complex.

## Slide 18: Thank you for listening
Alex.Valentine@ukaea.uk

## Slide 19: 175 group vs 5 group
Compare 5-group data we are using outside the bioshield to a finer 175-group which is available within the bioshield. The tool result using the two different group structures was compared. The results are ~37% different for this location, with 5-group overpredicting.
Differences related to the calculated effective cross section between the two group structures.
Compare the global maps of the effective cross section.
 | 5-g | 175-g | % diff
Tool, Atoms Co60 | 7.16E+16 | 5.2289E+16 | 37%
Effective xs | 5-g | 175-g
Co59 (n,g) Co60 | 1.36 | 1.12
Co59 (n,g) Co60m | 2.26 | 1.41
5-g/175-g effective cross section for Co59(n,g)Co60

## Slide 20: Comparison to FISPACT
A point was selected from the in-bioshield 175g radiation maps (900,900,0) and a FISPACT calculation performed irradiating 1kg of Cobalt for SA2 scenario with EAF2010 data. Tool run using the same xs data and selecting the same coordinate point and scenario.
  Verified that the correct flux was being extracted from the vtr by the tool.
  The effective cross section (collapse of flux & xs) were shown to be identical for the two reaction channels in cobalt (extract_xs in FISPACT can be used to output this).
  Compared the number of atoms at 12 days after shutdown of Co60 and the Co60 activity. Tabulated below – the results are within 1%.
Also checked at multiple locations and agreement shown to be within 1%
 | Tool | FISPACT II
Atoms | 5.2289E+16 | 5.2481E+16
Activity (Bq/kg) | 2.1699E+08 | 2.1869E+08

## Slide 21: Assumption of no-scattering
An MCNP calculation was ran with a Co-60 line source (one of the cryolines) just containing the outer walls of the NB cell (ITER concrete). The results for the dose using the reference DE/DF cards (ICRP-74) were compared between the concrete and void cases. Below plots the ratio of scattered/unscattered. The behaviour is as expected that the impact is greater at further distances from the source.