## Slide 1
Radiation transport model development with Gitronics applied to JT-60SA
Fusion Neutronics Meeting
April 2025
A. Cubi
alvaro.cubi@f4e.europa.eu

## Slide 2: Agenda
Radiation transport model development and management
Traditional methodology limitations
Novel methodology: Gitronics
  Modularization
  Git
  GitLab
JT-60SA reference model
Conclusions

## Slide 3
Radiation transport model development and management

## Slide 4: Radiation transport model development and management
ITER-like models' characteristics:
Large volume of parameters
Described in ASCII text
Single monolithic file
Several million lines long
Traditional management:
Reference model in continuous development (versions)
Changes are done in several parts of the huge monolithic file
Reference model as basis for assessments that may require specific modifications
Modifications may or may not end up in the new version

## Slide 5
Traditional methodology limitations

## Slide 6: Traditional methodology limitations
Monolithic input files
All information compressed in huge single file.
Difficult to understand and work with:
  Which tallies are active in this version?
  Where is the geometry of this diagnostic?
  Is this system featured or was removed/hidden?
Disorganization between collaborators:
  Same lines added by different people but millions of lines apart of each other.
Difficult to track differences between versions:
  300.000 lines of text added
  2000 lines modified
  5000 lines removed
  All changes spread throughout a 5 million lines file

## Slide 7: Traditional methodology limitations
Version Control issues
Collaboration barriers
Error tracking and reproducibility
Ref. 240101
Document Management System
Ref. 240101
TFC assessment
Ref. 240101
TFC assessment v2
Ref. 240101
TFC + PFC
Ref. 240101
TFC assessment v3
Ref. 240101 MOD
Ref. 240101
MOD No Meshtal

## Slide 8
Novel methodology: Gitronics

## Slide 9: Gitronics
F4E addresses the challenges of the traditional development and management approach with its novel methodology
The methodology is based on three technologies:
  Modularization via a dedicated Python package (developed in-house)
  Git
  GitLab
The development and management of radiation transport models now mirrors that of software development.
Industry-standard technologies, VCS and tools from the software development industry become available.
This workflow has been refined by the feedback of millions of developers during decades and received huge private investment.
Gitronics

## Slide 10
Gitronics: modularization

## Slide 11: Modularization
Dedicated Python package developed in-house
Acts as a sort of linker/compiler for MCNP files
The huge monolithic MCNP input can now be divided into a set of much smaller, single-responsibility files
The analyst works by adding or modifying small files and therefore:
  Changes between versions become easily identifiable
  The process is less error-prone
  The model is much easier to understand, work with, explain and audit.

## Slide 12: Modularization
Each system, tally, particle source, material definitions and other parameters can be their own single file
During the “compilation” of the MCNP input file, gitronics does:
  Select only the desired files according to a configuration file
  Orders each of the files according to card IDs and a standard
  Detects and warns of errors like:
    No particle source
    More than one particle source
    No tallies

## Slide 13: Modularization
V2.1.9
V2.1.9
Radmaps 2025
V2.1.9
Lost Particle check

## Slide 14
Gitronics: Git

## Slide 15: Git
Git is one of the most popular VCS in the software industry
Efficient version tracking and distributed development
Creates snapshots (commits) of the state of the project and all its files at specific points in time
Can revert to any previous version and to make comparisons between them
Favors a branching and merging approach that allows several people to work in the model while minimizing conflicts
Git can be used with the huge monolithic MCNP input file, but its effectiveness is greatly diminished
The gitronics package has been designed to maximize the usefulness of Git

## Slide 16
Gitronics: GitLab

## Slide 17: GitLab
Platform for software development that hosts Git repositories
Unlike GitHub, allows self-hosting
Collaboration features available in our private server without uploading anything to the Internet:
  Only a selected group of users can access the model
  Wikis for documentation
  Review capabilities
  Issue tracking
  Continuous integration

## Slide 18: GitLab

## Slide 19
JT-60SA reference model

## Slide 20: JT-60SA reference model: history
QST model
CAD
SuperMC
Mod_1. CAD
F4E legacy v1
Mod_2. CAD
GEOUNED
F4E legacy v2
GEOUNED
…
Traditional neutronics model management

## Slide 21: JT-60SA reference model: history
QST model
CAD
SuperMC
V0.0.0
V0.1.0
V1.1.1
Gitronics
Envelope-based Gitronics model development

## Slide 22: JT-60SA reference model: management

## Slide 23: JT-60SA reference model: management
vX.Y.Z

## Slide 24: JT-60SA reference model: enhancements
The main enhancements of the model with respect to the original QST model are:
Transition to a Gitronics methodology
Modular and envelope-based structure
Modeling and integration of main systems
  Cryostat base
  Opening of port penetrations in the cryostat
  Selected port extension definitions
Modeling and integration of diagnostics
  VUV
  TSS
  PLS
  TPCI
Correction of densities and material definitions to better approximate the expected masses as per latest designs
  VV cooling material
  Density correction factors (lower divertor, cryostat)
Standardization of format and syntax

## Slide 25: JT-60SA reference model: future work
Further development and maintenance of reference model.
Gradual substitution of homogenized components for detailed models:
  TFCs
  Central Solenoid
  STB
  …
Addition of detailed models of missing structures:
  Port Thermal Shields
  Common Stage
  Port extensions
Addition of diagnostics
  FILD
  Neutron spectrometers
  …
Calculation of updated radiation maps and dedicated responses.

## Slide 26
Conclusions

## Slide 27: Conclusions
F4E has developed and freely distributes the Gitronics package for neutronics model development.
Gitronics has already demonstrated significant benefits in the development of the JT-60SA model.
F4E has set up a private Gitlab repository for the JT-60SA model which is being actively developed.
Further enhancements envisioned for the JT-60SA model include:
  Addition of more structures and systems
  Substitution of homogenized components for detailed models
Contact: alvaro.cubi@f4e.europa.eu
Gitronics package: https://github.com/Fusion4Energy/gitronics