## Slide 1: Attila4MC® CAD Integrated Workflow for Fusion Neutronics Jonathan Rogers, Head of Software Development Silver Fir Software, Inc.

## Slide 2: About Attila4MC
Attila4MC provides MCNP® users with a CAD integrated workflow to streamline the Monte Carlo analysis cycle, from CAD through solution visualization
  Support of additional Monte Carlo codes currently under development (TBA late 2025)

## Slide 3: Attila4MC – Features and Benefits
Attila4MC - Helping users become more productive is our primary goal
Work directly with “real world” CAD assemblies
  No need for extensive CAD cleanup or simplification
  Modular functionality for rapid design iterations
Short learning curve and rapid calculation setup
  Intuitive Graphical User Interface (GUI)  Heavily commented MCNP input deck
Rapid solutions to complex, deep penetration problems
  Single-click CADIS/FW-CADIS weight window variance reduction with Attila4MC-CottonwoodTM
Intuitive visualization of 3D solution fields for valuable design insights
  Integrated solution visualization powered by Tecplot®

## Slide 4: CAD Integration with Attila4MC
Increasingly, Monte Carlo users are receiving complicated CAD assemblies with short analysis turnaround requirements
  Hundreds or thousands of CAD parts
  Many small part tolerance interferences
  Lots of detail not relevant to radiation transport calculations
Historically, CAD integration has required “clean” CAD models as input
  Clean CAD models are “unicorns”  they do not exist in practice
As a result, users are faced with the task of cleaning up and simplifying models for analysis
  Can take days or weeks of valuable engineering time

## Slide 5: CAD Integration with Attila4MC
Attila4MC provides a real-world CAD integrated workflow with the MCNP Unstructured Mesh capability
Largely eliminates the need for CAD cleanup or simplification
  No need to fix “insignificant” CAD part interferences/overlaps
  No need to remove small parts
  No need to simplify CAD part features
MCNP UM is tolerant of interferences
Production CAD assembly with interferences shown in red
R. Garoby et al., 2018 Phys. Scr. 93 014001

## Slide 6
CAD Integration with Attila4MC
Each part is meshed separately and joined at the end.
Global and part level controls, includes curvature refinement at the part level
Volume and surface analytics automatically produced to compare meshed volumes/surface areas to CAD.

## Slide 7
CAD Integration with Attila4MC
Robust – will not terminate when a part fails to mesh
  Failed parts can be re-meshed then joined in with rest of the model
Options to mesh only selected parts, rather than an entire assembly
Optional filtering of small parts
Modular for rapid design iterations

## Slide 8: CAD Integration with Attila4MC
Example Case – European Spallation Source (ESS) linac section
  6,822 parts, > 500 CAD part interferences
No CAD cleanup or simplification performed

## Slide 9: CAD Integration with Attila4MC
Less than 1 hour to produce “MCNP ready” Computational Mesh
  User Time: ~5 minutes (default settings used)
  Computational Time: ~30 minutes (36 core workstation)

## Slide 10: CAD Integration with Attila4MC
MCNP solution field from example case
Visualized in Attila4MC
  Tecplot® integrated into Attila4MC

## Slide 11: Calculation Setup With Attila4MC
Intuitive Graphical User Interface (GUI) Based Calculation Setup

## Slide 12: Calculation Setup With Attila4MC
GUI Features:
  Fixed source and k-eigenvalue calculations supported
  “Bill of Materials” feature to facilitate assignment of materials from CAD part names
  Integrated material database (PNNL-15870 Rev. 1, RJ McConn Jr et al.)
  Import feature for materials and source spectrums from legacy MCNP input decks
  Volume and point sources supported
  Tally creation for point, cell (region), and global solution visualization
  User defined edit cards for features not supported in the GUI
  Launch MCNP directly from the GUI or pack input for running on another machine
  Heavily commented input deck for easy user editing

## Slide 13: Attila4MC-Cottonwood
“Single-Click” Variance Reduction for the Most Demanding Applications
  Deterministic variance reduction for local or global solution fields (CADIS and FW-CADIS)
  Complex geometries with hundreds or thousands of parts easily handled
  Single-click default operation for most problems, with advanced controls for others
  Initial development funded by Commonwealth Fusion Systems
60Co source in 30cm iron cask, inside 100cm thick concrete wall. ~14 orders of magnitude attenuation to outside air.
MCNP – Analog
MCNP – Cottonwood

## Slide 14: Attila4MC-Cottonwood
Cottonwood Features:
  CADIS (local) and FW-CADIS (global) variance reduction modes
  Neutron, gamma, and coupled N-G calculation support
  Supports both volume and point sources
  Target tallies can be flux or response functions for point detectors, region(s), or full model
  Graphical user interface and command line modes
  Supports energy and spatial source biasing
  Automatic deterministic mesh generation (manual rectilinear options also provided)
  Automatic weight window grid generation (manual rectilinear options also provided)

## Slide 15
Attila4MC-Cottonwood
Deterministic calculations performed on an Adaptive Mesh Refinement (AMR) Grid
Incorporates adaptive spatial discretization algorithms
  Accurate and smooth solution fields for efficient weight window grids
Automated energy group optimization for calculation efficiency

## Slide 16: Attila4MC-Cottonwood
Cottonwood automatically generates the deterministic computational mesh, based on material half value layers (HVLs) and the prescribed source spectrum
  Automatically refines where needed, coarsens elsewhere  minimizing elements and calculation time
Enables rapid deterministic calculation for weight window generation, and efficient Monte Carlo calculations, all with minimal user effort
Cottonwood auto-generated computational mesh for weight window generation, showing adjoint solution field
MCNP solution field using Cottonwood generated weight windows

## Slide 17
Attila4MC-Cottonwood

## Slide 18: Questions?
Contact us at support@silverfirsoftware.com