## Slide 1
Fusion Neutronics Developments for Fusion Reactor Design and Assessment (FREDA)
APRIL 2025
Jin Whan Bae, Katarzyna Borowiec, Arpan Sircar, Vittorio Badalassi, Cami Collins
Oak Ridge National Laboratory

## Slide 2
Fusion Energy Reactor Models Integrator (FERMI) Fusion Reactor Design and Assessment (FREDA)

## Slide 3
Uncertainty quantification is one of the focus areas
Uncertainty quantification of two levels:
  Assessing the level of fidelity for an accurate but computationally efficient workflow
    E.g., Mesh refinement study – how many energy groups are sufficient for an accurate activation calculation ⟷ computational efficiency

## Slide 4
Uncertainty quantification is one of the focus areas

## Slide 5
Uncertainty quantification is one of the focus areas
Uncertainty quantification of two levels:
  2. Impact of things that we don’t actually know well
    E.g., nuclear data uncertainty propagation

## Slide 6
Uncertainty quantification is one of the focus areas
Extending uncertainty propagation to coupled analyses like computational fluid dynamics (CFD)

## Slide 7
FREDA is modular
The CAD + materials csv → Full input set
Neutronics automation

## Slide 8
(somewhat) Code-agnostic
  Standardized input format → code-specific input files
Other helpful modules:
  Activation module
  Exporting to other formats (VTK, OpenFOAM)
Neutronics automation

## Slide 9
Enables automated perturbation runs
  Design space exploration
  Optimization
OpenMC is mostly used for FREDA
Neutronics automation

## Slide 10: Added parametric geometry generation (Katarzyna Borowiec)

## Slide 11: Previous works: Exploring impact of material dimension and composition for tokamaks
Multi-dimensional sensitivity study for various material and design choices for Tokamak

## Slide 12: Previous works: Exploring impact of material dimension and composition for tokamaks
TBR response to material thickness / selection is dependent on other configurations
  E.g., Be multiplier increases TBR only if Li enrichment is high AND vacuum vessels are thin enough
  Designing for increase in TBR can lead to increased specific activity of vacuum vessel

## Slide 13: Previous works: Automated optimization of tokamak geometry
Wrap the entire neutronics workflow to an optimization driver to automate design space exploration

## Slide 14: Previous works: Automated optimization of tokamak geometry

## Slide 15
Nuclear data uncertainty propagation – Total Monte Carlo
Develop SANDY–OpenMC coupling
Use any full OpenMC input XML files to generate N random nuclear data library samples

## Slide 16
Nuclear data uncertainty propagation – Total Monte Carlo
Tested for Jezebel (critical sphere)
  Uncertainty (standard deviation of metric) is similar to existing code:
    TSUAMI-IP: 598.19 pcm
    OpenMC TMC: 571.01 pcm
Too computationally heavy for regular analyses

## Slide 17
Nuclear data uncertainty propagation – Sensitivity coefficient
Pursuing multiple avenues
  MCNP
    Using PERT cards
  Shift
    SCALE nuclear data sensitivity functionality (TSUNAMI)
  OpenMC

## Slide 18
Impact of activation metrics with operational modeling
  Constant, scaled, explicit
Leveraging experience from molten salt reactors, in which the fuel flows in and out of the core
Pulsed operation modeling impact on activation

## Slide 19
'Scaled' is a computationally optimal approach to activate pulsed-operation activation
Pulsed operation modeling impact on activation

## Slide 20
Neutronics coupling

## Slide 21
OpenMC unstructured mesh tally → VTK → OpenFOAM mesh and data files
Impact of pulsed operation + decay heat for transient modeling
Pulsed operation modeling impact on CFD

## Slide 22
Decay heat is obtained at 2 Effective Full Power Years (EFPY) for tetrahedral mesh
Pulsed operation modeling impact on CFD

## Slide 23
CFD results → Neutronics mesh → sub-OpenMC-cells
KMeans clustering for subdomain creation
  Splitting one OpenMC ‘cell’ to multiple ‘cells’
Automated material and property labeling to OpenMC file generation
Neutronics–CFD coupling feedback modeling
CFD result

## Slide 24
Neutronics–CFD coupling feedback modeling
CFD result, N=1 vs N=25 for each region

## Slide 25
Little observed bulk TBR difference if volume-average temperature and density are constant
Neutronics–CFD coupling feedback modeling

## Slide 26
Local tritium-breeding reaction (~flux) rates vary up to ~4%, only on the outer edges
Difference is calculated by:
  (TBRN=1 – TBRN=25) / TBRN=1
Neutronics–CFD coupling feedback modeling

## Slide 27: Coupled neutronics and CFD enable tritium tracking in FREDA workflow
Achievement
Neutronics and CFD were coupled to get spatially resolved tritium generation
CFD capabilities were extended by adding equation to solve for tritium diffusion & convection with time-dependent source term
This could be extended to other species transport problems (e.g., ACP, gamma source)
Significance and Impact
Enables tracking of tritium within the blanket to improve understanding of breeding, containment, and extraction.
  Where does tritium end up? How much does buoyancy, MHD, etc. matter?
  Is TBR sufficient after accounting for loss terms (absorption, loss, radioactive decay, etc.)?
Research Details
Neutronics (openMC or MCNP) is used to get heat deposition and tritium generation, then mapped to OpenFOAM
Future work: Include more physics to account for tritium diffusion in solids (including SLAG).
Fickian diffusion
Soret diffusion
Difference in tritium concentration with & without Soret effect
BT=0
BT=10 T
Arpan Sircar
tritium production rate
MHD affects flow (tritium trapping?)

## Slide 28
Comparison of FISPACT-II, ORIGEN, and OpenMC (depletion only)
Standardized workflow to automate simulation for both ORIGEN and OpenMC
Insights:
  OpenMC
    Reaction nuclide yield data is important
    Flexibility of nuclear data is important
  SCALE/ORIGEN
    Identified missing isotopes in decay data
OpenMC activation validation for Fusion Neutron Source benchmark

## Slide 29
OpenMC
  Reaction nuclide yield data is important
    JEFF3.3_noyield is wrong because it only considers Ag107 → (n,gamma) → Ag108
      But it also yields Ag108m, as an energy-dependent yield
    More common in faster energies
    Fixed by generating custom chain files for flux spectrum
  Flexibility of nuclear data is important
    TENDL2019 outperforms older libraries
OpenMC activation validation for fusion neutron source benchmark

## Slide 30
SCALE/ORIGEN
  Identified missing isotopes in decay data
    K38 and F18 missing in decay data for ORIGEN
    Isotopes occurring in threshold reactions
    Reported to SCALE developers (will be patched in next version)
OpenMC activation validation for fusion neutron source benchmark

## Slide 31
Development efforts to:
  Provide comprehensive engineering analysis of fusion device
  Develop streamlined workflows for advanced analysis or design optimization
Working to release this to public
Conclusion