## Slide 1
Shutdown dose rate evaluation for the beam dump in the Linear IFMIF Prototype Accelerator (LIPAc) with Direct 1 Step MCNP
K. Kumagai, QST-Rokkasho, Japan
Fusion Neutronics Meeting 2025: ITER and beyond
Facultad de Educación of UNED
7 – 10 April

## Slide 2
Linear IFMIF Prototype Accelerator: LIPAc
A FNS requires high neutron flux (1016 n/cm2/s in avg) & high availability (70%).
Fusion neutron source (FNS) is required for material testing for DEMO reactor.
The LIPAc is targeting a world-class-high-current deuteron beam (125 mA) with 9 MeV in continuous wave operation as those are required for the FNS.
Injector
Radio-Frequency Quadrupole (RFQ)
Full length of LIPAc. 5 MeV D+, 125 mA, Achieved 8.75% Duty cycle
in Phase B+ campaign (2019 Winter – 2024 Summer)
Beam direction
MEBT
MEBT Extension Line
High Energy Beam Transport (HEBT)
Beam Dump (BD)

## Slide 3
LIPAc Beam Dump
Intense deuterons of [d/s] (125 mA) are bombarded into the Copper cone.
Secondary neutrons are generated by nuclear reactions of Cu(d,xn).
The deuterons only activate Cu cone due to the short range in copper, which is 50 m for 5 MeV and 130 m for 9 MeV, while the Cu cone thickness is around 5 mm.
These secondary neutrons can activate not only Cu cone, but also SS pipes, Fe, concrete.
Beam
Cu cone target
Polyethylene (for neutron)
Iron shield (for gamma)
SS pipe

## Slide 4
Shutdown dose rate around the beam dump
Estimate the shutdown dose rate (SDR) around the beam dump for the maintenance after the beam operation.
This study uses Direct 1 Step (D1S) method for neutrons because Rigorous 2 Step (R2S) method requires an approximation by meshing MCNP cells for neutron flux.
Objectives
Calculation method for SDR
Understand the relationships among SDR, the deuteron beam energy, beam time, cooling time to develop the beam operation senario.
The SDR due to deuterons because of activation of Cu cone, such as Cu-65(d,2n)Zn-65, is also separately calculated.
Cu cone target is
inside the SS pipe

## Slide 5
Neutron intensity by Cu-d reaction
Neutron intensities due to Cu-d nuclear reactions are calculated for D1S MCNP calculations in the case of 5 MeV and 9 MeV deuterons using a simple axisymmetric geometry.
5 MeV (D+)
9 MeV (D+)
Calculation results on Double differential neutron thick target yield
Cu (t:0.2mm)
Neutron flux (Cu-d: 5 MeV/9MeV)
tally (5-degree mesh)
JENDL-5 deuteron sublibrary is used for the neutron yield calculations.
Total neutron intensities are n/s and n/s for 5 MeV and 9 MeV deuterons, respectively.

## Slide 6
Nuclear reaction selection for D1S
Nuclear reactions considered in D1S MCNP calculation
Using FISPACT-II with TENDL-2017, nuclear reactions considered in D1S are selected by calculating activation of Cu cone, SS pipes, Fe shield, and concrete using the real chemical compositions.
Cu-64, Co-60, Mn-56, Na-24 to be problematic radionuclides for the shutdown dose rate.

## Slide 7
D1S result: Shutdown dose rate
Case: 5 MeV, Beam = 104 s, Cool = 104 s
The SDR around the tip of Cu cone: 1 Sv/h.
Activation due to neutrons contributes to the SDR more than deuterons (in this case).
Point A
*SDR along the beam axis.
More cooling is necessary for hands-on maintenance of Cu cone considering ICRP recommendation: 50 mSv/year (for Rad-workers).
But, How long cooling…?
Cu-64 ( = 13h) mostly contributes to the SDR.

## Slide 8
Decay of shutdown dose rate
SDR decay with cooling time (Operation time = 104 seconds)
200 Sv/h
(5MeV)
40 mSv/h
(9 MeV)
*ICRP rec: 50 mSv/year (Rad-workers).
After 106 seconds (~10 days) from operation:
5 MeV operation: 200 Sv/h
Acceptable. Hands-on maintenance is possible for several days.
9 MeV operation: 40 mSv/h
Not acceptable.
Because of 350 times larger Zn-65 production than 5 MeV.
Additional local shield or remote handling to be necessary for the beam dump maintenance.
Also, need to consider the operation strategy.

## Slide 9
Summary
The shutdown dose rate (SDR) has been estimated for the beam dump in an intense 125 mA deuteron accelerator, LIPAc, using Direct 1 Step (D1S) method for secondary produced neutrons by Cu-d nuclear reactions.
In the case of continuous beam operation for 104 seconds, a cooling time of 104 seconds is sufficient for 5 MeV for the maintenance, however, it is insufficient for 9 MeV as additional shields and/or remote handling would be required.
The relationships among the SDR, beam energy, operation time, and cooling time have been examined to develop the beam operation senario and the beam dump maintenance strategy.

## Slide 10
Thank you !

## Slide 11
Neutron flux around beam dump
Beam direction
Vertical section (neutron flux)
Cu cone
Concrete wall
Iron
PE
SS pipe
Beam dump geometry is modeled manually by defining Cu cone, Fe cylinder, etc.
Neutron flux is calculated for selecting nuclear reactions which contribute to SDR.
Beam direction
Horizontal section (n-flux)
Bending magnet
(Dipole)

## Slide 12
Chemical compositions of BD materials
Cu cone
Concrete
Iron shield
SS pipe
Actual chemical compositions are used for Cu cone, SS pipe, and Fe shield.
For concrete, the chemical composition in literature is used.
Activation of additive & impurity elements (Mn, Co,…) can also be important for SDR as described later.

## Slide 13
D1S result: Radionuclides production
Result in the case of 5 MeV deuteron. Beam time = 104 seconds, Cooling time = 1 second.
The contour shows the shutdown dose rate per neutron intensity for each radionuclide.
Na-24 (=15h)
Cu-64 (=13h)
Al-28 (=2.2m)
Mn-56 (=2.6h)
Co-60 (=5.3y)
Mo-101 (=15m)

## Slide 14
D1S result: Shutdown dose rate
Material activation due to neutrons contributes to the SDR more than that due to deuterons in this case.
This SDR also considers the activation of Cu cone due to deuterons (e.g. Cu-65(d,2n)Zn-65)).
Case: 5 MeV, Beam = 104 s, Cool = 104 s
The SDR around the tip of Cu cone: 1 Sv/h.
Point A

## Slide 15
SDR vs Beam energy, Cooling & Operation times
In the case of 9 MeV deuteron, the shutdown dose rate is 350 times larger than the case of 5 MeV deuteron at a cooling time = 106 s, because of Zn-65 production.
Because the influence of long-half-life radionuclides, such as Zn-65 and Co-60, gets significant, completing beam commissioning by smaller beam energy is quite important.
Point A
SDR decay with cooling time
(Operation time = 104 seconds)
Point A
SDR increase with operation time (Cooling time = 106 seconds)
Point A

## Slide 16
Zn-65 Production
TENDL-2017