## Slide 1
Fusion Neutronics Meeting
April 10, 2024
P. Guijosa1, J. Alguacil1, G. Pedroche1,2, R. Juárez1 & P. Sauvan1
1Universidad Nacional de Educación a Distancia (UNED)
2Universidad Politécnica de Madrid (UPM)
Study of the D1SUNED transport subroutines for future optimizations in benefit of ITER nuclear analyses

## Slide 2: Introduction
In the last decade, the MCNP models used in ITER nuclear analyses have evolved significantly
Tokamak Models
(Partial)
Tokamak Complex Models
(Radmaps 2016 & 2020)
E-lite (360º)
ITER full model (prototype)

## Slide 3: Motivation
Since 2022, the UNED team has been working on the design of an ITER integral representation.
However:
The computational complexity of these models has been increasing:
  More surfaces
  More cells
  More materials
Although the UNED team has improved D1SUNED in the past:
  We need more improvements and optimisations
Computational
demand
Transport is demanding
Even with HPC infrastructures, using integral representations for the ITER nuclear analyses seems challenging
We studied the time consumption of the transport subroutines of D1SUNED for future optimisations

## Slide 4: Methodology
Heterogenous C-model
Homogenised C-model
Using E-lite
Using a homogenisation tool

## Slide 5: Transport in the HET model
Action | Time (min) | % Transport
chkcel | 1214.04 | 3.00
track | 14376.60 | 35.56
surfac | 14913.84 | 36.89
Collisions | 795.37 | 1.97
Bank | 733.48 | 1.81
N data | 4172.39 | 10.32
P data | - | -
Transport | 40431.03 | 100.00
- The 75.45% of the N transport time is spent by the geometry subroutines.
Time consumptions by the transport algorithm
for N transport using the HET model
Action | Time (min) | % Transport | Time NP/N
chkcel | 7626.39 | 2.81 | 6.28
track | 71891.55 | 26.46 | 5.00
surfac | 34471.78 | 12.69 | 2.31
Collisions | 9005.19 | 3.31 | 11.32
Bank | 116561.11 | 42.90 | 158.91
N data | 4509.49 | 1.66 | 1.08
P data | 12182.84 | 4.48 | -
Transport | 271732.08 | 100.00 | 6.72
Time consumptions by the transport algorithm
for NP transport using the HET model
- The 42.90% of the NP transport time is spent by the increase in the number of accesses to the secondary particle bank.

## Slide 6: Transport in the HOM model
In the case of the HOM model:
- In mode N, the geometry subroutines and the load of N nuclear data consume 34.62% and 38.44%. The bank accesses cosumes a 2.69%.
- 55.70% of the NP transport time is spent by the accesses to the secondary particle bank.
What did we do?
MODE N
MODE NP
HET model
MODE N
MODE NP
HOM model
What can we do?
MODE N
MODE NP
HET model
MODE N
MODE NP
HOM model

## Slide 7: Transport in HET vs. HOM
Action | Time (min) | % Transport | Time HOM/HET
chkcel | 662.51 | 3.69 | 0.55
track | 4359.91 | 24.27 | 0.30
surfac | 1195.74 | 6.66 | 0.08
Collisions | 594.87 | 3.31 | 0.75
Bank | 483.46 | 2.69 | 0.66
N data | 6903.79 | 38.44 | 1.65
P data | - | - | -
Transport | 17960.95 | 100.00 | 0.44
Time consumptions by the transport algorithm
for N transport using the HET and the HOM model
Action | Time (min) | % Transport | Time HOM/HET
chkcel | 3975.39 | 2.29 | 0.52
track | 23223.73 | 13.36 | 0.32
surfac | 4577.23 | 2.63 | 0.13
Collisions | 7282.71 | 4.19 | 0.81
Bank | 96820.03 | 55.70 | 0.83
N data | 7091.96 | 4.08 | 1.57
P data | 16752.42 | 9.64 | 1.38
Transport | 173824.28 | 100.00 | 0.64
Time consumptions by the transport algorithm
for NP transport using the HET and the HOM model
- Transport time is reduced.
- The geometry subroutines are called less times and faster (x0.20 in mode N, x0.28 in mode NP).
It accelerates the simulations
Bank accesses and collisions decrease.
- Each load of nuclear data is more expensive.
Drawback?

## Slide 8: Potential drawback
Component | Total | Neutrons | Photons
Blanket | 1.78 | -14.09 | 6.67
Divertor | -8.98 | 25.12 | -15.32
Vacuum Vessel | -53.10 | 0.21 | -62.57
TFCs | -40.20 | -32.72 | -40.99
PFCs | 120.37 | 132.32 | 118.82
Relative deviations (%) of the NH tallies by contribution
Does it entail a cost? We analysed Nuclear Heating (NH) tallies:
The potential drawback is the distortion of the radiation fields forecast

## Slide 9: To sum up
Increase of the computational demand
Transport phase is computationally expensive
It seems challenging to use integral representations
We studied the D1SUNED transport subroutines time consumptions
Results with HET model allowed to conclude:
The geometry subroutines are the main consumers for the N transport
Accesses to secondary particle bank are for the NP transport
Simplifying cells descriptions would be good too
We systematically demonstrated that the homogenization works as an acceleration technique
However, it may entail the distortion of the radiation fields forecast

## Slide 10: Thank you for your time!

## Slide 11: Additional slides

## Slide 12: Models
Integrated parts from E-lite to the C-model
Region of the C-model | Integrated part of E-lite
Blanket Modules | Detailed Blanket Modules
Equatorial Port #11 | Representative Diagnostics Equatorial Port
Equatorial Port #12 | Diagnostics Equatorial Port #12
Equatorial Port #13 | Ion Cyclotron Heating system
Upper Port #11 | Representative Diagnostics Upper Port
Upper Port #12 | Electron Cyclotron Heating systems
Upper Port #13 | Electron Cyclotron Heating systems
Homogenisation workflow:
Homogenised Blanket, Divertor, Vacuum Vessel, TFCs and PFCs

## Slide 13: Calls to the subroutines
Action | N transport | NP transport | NP/N
Collision | 9.88e9 | 4.88e10 | 4.94
Bank | 6.79e7 | 1.08e10 | 159.40
Calls to the bank and the collisions subroutines using the HET model
Action | N transport | NP transport | NP/N
Collision | 7.41e9 | 4.03e10 | 5.44
Bank | 4.64e7 | 9.04e9 | 194.75
Calls to the bank and the collisions subroutines using the HOM model
Action | HET | HOM | HOM/HET
chkcel | 9.55e9 | 7.09e9 | 0.74
track | 1.69e10 | 8.81e9 | 0.52
surfac | 2.39e10 | 1.02e10 | 0.43
Collision | 9.88e9 | 7.41e9 | 0.75
Bank | 6.79e7 | 4.64e7 | 0.68
N data | 1.44e10 | 8.18e9 | 0.57
Calls of subroutines for the N transport
Action | HET | HOM | HOM/HET
chkcel | 4.73e10 | 3.88e10 | 0.82
track | 7.93e10 | 4.60e10 | 0.58
surfac | 1.10e11 | 5.16e10 | 0.47
Collision | 4.88e10 | 4.03e10 | 0.83
Bank | 1.08e10 | 9.04e9 | 0.84
N data | 1.44e10 | 8.18e9 | 0.57
P data | 5.48e10 | 3.56e10 | 0.65
Calls of subroutines for the NP transport

## Slide 14: Homogenization results
Component | HET | HOM | Rel. Dev. (%)
Blanket | 4.56e7 | 4.64e7 | 1.78
Divertor | 5.98e6 | 5.44e6 | -8.98
Vacuum Vessel | 2.05e6 | 9.59e5 | -53.10
TFCs | 3.32e3 | 1.98e3 | -40.20
PFCs | 1.04e2 | 2.30e2 | 120.37
NH (in Watts) results for N and P
Component | HET | HOM | Rel. Dev. (%)
Blanket | 1.08e7 | 9.24e6 | -14.09
Divertor | 9.37e5 | 1.17e6 | 25.12
Vacuum Vessel | 3.08e5 | 3.09e5 | 0.21
TFCs | 3.16e2 | 2.13e2 | -32.72
PFCs | 1.20e1 | 2.78e1 | 132.32
NH (in Watts) results for N
Component | HET | HOM | Rel. Dev. (%)
Blanket | 3.49e7 | 3.72e7 | 6.67
Divertor | 5.04e6 | 4.27e6 | -15.32
Vacuum Vessel | 1.74e6 | 6.50e5 | -62.57
TFCs | 3.00e3 | 1.77e3 | -40.99
PFCs | 9.24e1 | 2.02e2 | 118.82
NH (in Watts) results for P