## Slide 1: Point-kernel-based 3D ray tracing gamma dose rate calculator
Gábor Náfrádi
IO/ESD/NSE
gabor.nafradi@iter.org

## Slide 2: Outline
Problem description
Methodology
GUI and Input preparation
Ongoing developement
Pros and cons

## Slide 3: Problem description
At ITER there is a complex time dependent neutron and gamma radiation field which is modeled with MCNP based simulations as standard
This method is robust and accurate but demands significant time for model preparation/runtime/post processing
However some of the components of the radiation field may be modeled with other means:
  Point kernel based 3D ray tracing for discrete decay gamma sources like: TCWS 16N or ACP sources
  To have a tool where easy to check design changes, assess uncertainties independently

## Slide 4: Methodology
3D point kernel method for dose rate calculation (monoenergetic):
  Where denotes the target point, F is an arbitrary factor, DCF is the dose conversion factor, denotes the source points, I is the intensity at each given source points, denotes the distance between and , denotes the density of the ith material, denotes the mass attenuation coefficient of the ith material and denotes the thickness of the ith material
To determine the the open source python ray tracing is used with stl geometry files

## Slide 5: Methodology
can be obtained from https://www.nist.gov/pml/x-ray-mass-attenuation-coefficients
DCF values can be adjusted to values used in MCNP calculations
is an user input, for examplele the 16N intensity along pipes
values can be adjusted to the values used in MCNP calculations
is trivial as the target and source points are all user inputs

## Slide 6: GUI and Input preparation
User can restrict the source and target ROI
Source points and intensities as csv e.g.:
x,y,z,intensity
2619.00259,1680,1433,1.22E+16
Target points as csv
Each material should be represented by a separate stl file
-Watertight, avoid overlapping regions
-it is possible to assign the density and mass attenuation coefficient for each material (geoemtry)
-F factor can be used, for build up or for safety factor
-DCF for the gamma energy of interest
-The VOID not defined in the geometry files is assumed to be air Air mass attenuation coefficient*Air density should be set

## Slide 7: PRELIMINARY! Output example
Output is a vtk file
Performance for
24 source points at UPC
18928 target points:
~3.5 hours with 8 cores
Using geometries:
-TKC NC structures,
-TKC HC structures,
-TKC Steel structures
-Backfilling+cable tray

## Slide 8: Ongoing developement
Multiple energy line handling
Energy and material dependent build up handling with e.g.:Geometrical Progression
Cluster compatibility
Input deck save and load
To have a standard code for 16N and 60Co but still keep flexibility of the code
Goal is to have the new version by the end of the year

## Slide 9: PRELIMINARY!
Performance
12 Energy lines of 16N
1718 source points at UPC
15300 target points:
~43 hours with 8 cores
Using geometries:
-TKC NC structures,
-TKC HC structures,
-TKC Steel structures
-Backfilling+cable trays
-TCWS pipes
-TCWS water
-TCWS lead
-TCWS Novashield
-TCWS concrete
Point kernel based, no build up, Z=1308 cm
Radmap2020, IBED 16N dose rate, Z=1308 cm
source

## Slide 10: Pros and cons
Pros:
  Independent method from MCNP
  3D CAD geometry, no difficult geometry preparation
  No special expertise is needed to use the code
  Significantly less computational cost is foreseen
  Quick results, for design or for comparative studies
  May be used for error estimates
  Point source approximation
Cons:
  Limited to gamma
  Some phenomena can’t be modelled (skyshine, backscattering)
  Point source approximation (more accurate for large distances)
  Build-up approximation

## Slide 11
Collaborators are welcomed!