## Slide 1: Supply and Demand of Tungsten for a Fleet of Fusion Reactors
E. Day-San [a], Gabriel Blackett [a] M. Dornhofer [b], A.K. Manduku [a], M.D. Anderton [a], L. Tanure [a], T.P. Davis [a, c]
[a] Oxford Sigma, Summertown Pavilion, 18-24 Middle Way, Summertown, Oxford OX2 7LG
[b] Independent Supply Business Partner, Bluetengasse 9, A-8010, Graz, Austria
[c] Nuclear Futures Institute, Bangor University, Bangor, Gwynedd, LL57 2DG, UK
www.oxfordsigma.com
, , , , , ,
, , , , , ,

## Slide 2
Our Mission
To deliver materials technology, materials solutions, and fusion design services
Fusion Materials Engineering
Qualification of fusion pressure vessels leading the ASME BPVC Section III Division 4 “Fusion Energy Devices”​ code
Leading Fusion Component Design such as first-wall structures and blankets​
Experts on radiation damage in functional and structural materials

## Slide 3: Publication
Sections taken from publication in Fusion Engineering and Design, February 2025
Thanks to Guardian Metal Resources and Tungsten West.
Fusion Industry Program funded students: Elektra Day-San and Ariana Manduku.
Further thanks to Micheal Dornhofer of ISBP for insight into the tungsten mining industry.
https://doi.org/10.1016/j.fusengdes.2025.114881

## Slide 4: Tungsten supply uncertainty for fusion
Tungsten is a leading material for plasma facing and shielding.
Degradation of mechanical and thermal properties under neutron irradiation.
Uncertainty in operational lifespan – limited experimental data in fusion relevant conditions.
Supply Chain Uncertainties
Global production estimated at 78,000 tonnes per year.
Competing industries: Automotive, Defence, Hardware.
Geopolitical & Market forces: Domestic supply chain security a concern.
Yearly tungsten production (tonnes) by country. Source: USGS
Leading plasma facing material due to its unique combination of favourable properties. It finds application in fusion as: plasma facing component (first wall, and divertor), radiation shielding, and protective coatings
Advantages
High melting temperature (3422 C) and thermal conductivity (173 W/m.k)
Low neutron activation (absorption cross section 0.1-1b) and low sputtering threshold energy (25-50 eV)
Low tritium retention
Excellent mechanical properties at high temperatures
Low thermal expansion coefficient (4.5 µm/m C)
Disadvantages
Brittle at room-temperature
High ductile-to-brittle transition temperature (DBTT)
Recrystallisation-induced embrittlement
Neutron-irradiation-induced embrittlement

## Slide 5: The paper aims to..
Mining
Existing Availability
Expansion & Investment
Extraction and Processing Rates
Fusion Demand
Manufacturing
Production Rates
Manufacturing method advancements
Competing Sectors
Market
Foreign & Domestic Policy
Economic Viability of Extraction
Component Replacement Rate
Reactor Construction Rate
Overnight Construction Demand
….Identify these
….Model these
Supply
Demand

## Slide 6: Reactor configurations considered
ARIES-ST
EU-DEMO1
Spherical tokamak – “A U.S. national effort with participation from national laboratories, universities and the industry, and with strong international collaborations.
Tungsten plasma facing armour
Steel structure
Lead – lithium (LiPb) blanket, eutectic (83% Pb, 17% Li)
Conventional tokamak from an EU design effort.
tungsten plasma facing armour.
Steel blanket and vacuum vessel structure.
(Likely) LiPb
Characteristics
https://doi.org/10.1016/j.fusengdes.2005.11.003
https://doi.org/10.1016/j.fusengdes.2015.05.027
At this stage, these two reactor types have been considered. Additional reactor types may be considered in future depending on the availability of information found in public literature.
OS’ investigation has selected radial build thicknesses and material volumes to be used in neutronic analysis as seen below.
Shielding Materials: “ITER-Grade” W, WC, W2B
Reactor Power: 2000MW
Tungsten Components: First Wall, Central Column Shield, Divertors, Rear Blanket Shield.
Paramak implementation
Paramak implementation

## Slide 7: Methodology
Paramak 0.8.8
DAGMC
OpenMC 0.14.0
Mass & Roll Out Model
Damage energy tallied and dpa/fpy extrapolated.
Lifetime calculation: components considered replaced after reaching dpa limit.
Lower 2 dpa limit – Based on expected full loss of tungsten ductility under operating conditions.
Upper 4 dpa limit – Estimation, uncertainty in material data.
Component considered ‘replaced’ when limit reached. Consumption extrapolated over full reactor lifetime of 40fpy
A near-complete loss of ductility takes place for W irradiated at 400–500 °C to <2 dpa. Y. Katoh, et al., Response of unalloyed tungsten to mixed spectrum neutrons, J. Nucl. Mater. 520 (2019)
Notes: Tungsten percentage by ao
FW
Central Column Shield
Divertors
Rear Blanket Shield

## Slide 8: Key Findings: Aries-ST (2000MWth)
Rear shield replaced after ~25fpy, but negligible due to overall consumption
Total
Total
ITER-W Best Performing: High mass at install offset by lower replacement rate, Average 23,117 tonnes / 40 fpy
WC Worst Performing: Lower initial install but highest replacement rate, Average 35,998 tonnes / 40-fpy
Central column shield largest consumer
Rear shield lifetime component
~55% increase in tungsten consumption over pure W

## Slide 9: Key Findings: EU-DEMO1 (2000MWth)
If considering a 2dpa limit, shields required replacement after ~30fpy
W2B Best Performing: Similar replacement rate but lower mass than ITER-W. Average tonnes 9012 / 40 fpy
WC Worst Performing: Required replacement of rear shield Average 10,172 tonnes / 40 fpy
First wall dominant consumption
Total
Total
Central column and rear shield
Lifetime components
Full Power Years
Full Power Years

## Slide 10: Roll Out Comparison
Roll out model – Based on N. J. Lopes Cardozo et. al market adoption model for new energy sources.
Deployment model with 3 phases.
Fission ~9% of current global energy market share
Phase 2: Linear Growth
Phase 3: Saturation
Phase 1: Exponential
Growth
Model for expansion of emerging energy technology

## Slide 11: Roll Out Model
Phase 1: Exponential
Growth
Phase 2: Linear Growth
Phase 3: Saturation
World energy production estimated at ~30TW by 2100
Saturation determined by number of fusion reactors to supply 10% of the worlds power by 2100 (~3TW).
Consumption continues after saturation due to component replacement & replacement of reactors after 40fpy.
15,000 reactors required under U.S. DoE FPP 200MWe definition.
3,279 reactors required using 915MWe FPP definition.
Comparison with fission

## Slide 12: Key Findings: Average Total Tonnage
Derivative of S-curve taken, summed
Models considered a 50/50 EU-DEMO, Aries-ST roll out.
By 2100:
1.26 million tonnes per year (4dpa limit)
2.25 million tonnes per year (2dpa limit)
Average yearly replacement demand of 580 tonnes
Large contribution by Aries-ST (941 tonnes) vs Demo (221 tonnes).
Contributes to 1.9 million tonnes per year by 2100.
Roll out model provides average of 73 new installed reactors per year at average install mass of 2074 tonnes
Contributes to ~230,000 tonnes per year.

## Slide 13: Key Findings: Optimal Roll Out
100% 2000MWth EU-DEMO1 roll out – Most power to mass efficient design.
By 2100….
1.26 million tonnes per year (2dpa limit)
840,000 tonnes per year (4 dpa limit)
Comparison to 3 example scenarios
“Stagnant” - Current global production (~78,000 tonnes per year)
“Limited” – Exclusion of Chinese & Russian supply (~13,000 tonnes per year)
“New Generation” – Heavy Western investment in domestic tungsten extraction
Scenario 1 & 2: Tungsten demand exceeds current supply in the 2050s.
Scenario 3: Requires ~400,000 tonne increase in yearly production by 2060.
*Assumes no other competing industries or slow in demand due to market/supply constraints.
~97x increase
~17x increase
Across all material designs
Avg 157 tonnes in replacements per year
Avg 3269 tonnes install mass

## Slide 14: Conservative Considerations
Fission-like roll out
Peak 44 new reactors per year * 3269 install tonnes = 143,836 tonnes per year
440 total reactors * 157 replacement tonnes per year = 69,080 tonnes per year
Current global production – 78,000 tpy
‘Western’ production – 13,000 tpy

## Slide 15: Resource Considerations
Hemerdon Mine, UK
2,800tpy
Multiple operations, Russia
~10,000 tpy
Bakuta Deposit, Kazakhstan
~7,700 tpy
Sangdong Mine, S. Korea
1,750tpy
King Island Mine, Aus
~1,850 tpy
~30,000 total tonnes
Pilot Mountain, Nevada, USA
Upcoming and potential tungsten sources - USGS.
Supply ≠ Reserves
Short term increases in demand can be covered by large reserves.
Lead times on new operations
~5-year minimum between investment decision and the commencement of production.
Mining vs Processing & Manufacturing
Countries may have large raw resources but little capacity to process.
Offtake Agreements
Agreement mining and processing operators can ensure secured supply and stabilised prices.
Notes: Who have capabilities to manufacture tungsten – Japan, China,
China largest producer of raw tungsten but imports large fraction of tungsten-carbide goods.
USA maintains large reserves but no operational mines.

## Slide 16: In the context of a fusion timeline

## Slide 17: Conclusions
Higher fidelity models & greater uncertainty assessment
Include maintenance schedules
Include manufacturing supply and bottlenecks
Apply other critical minerals and supply chains
(HTS, Eurofer, lithium breeders)
Next Steps
Tungsten consumption was estimated in D-shaped and Spherical tokamak designs.
Aries-ST: ~23,000 tonnes over 40fpys (Pure W shield)
EU-DEMO: ~9000 tonnes overs 40fpy (W2B shield)
Accounting for replacement rate of components and upfront cost of reactor deployment
‘Optimal’ DEMO roll out looks to exceed current tungsten production capabilities.
Robust supply chains likely need large development.
EU-DEMO1
Aries-ST

## Slide 18: Thank you for your time