## Slide 1
Speeding up complex MCNP simulations using neural network source biasing
Elena Martínez Fernández*, Rafael Juárez, Javier Alguacil *emartinez@ind.uned.es

## Slide 2
A bit of context
Monte Carlo simulations are essential for neutron transport analysis in nuclear reactor. Specific challenges that affect the accuracy of the tally results.
Variance reduction techniques are essential to make Monte Carlo simulations more efficient. Without VR, simulations need a very high NPS Applying VR is challenging  source biasing, which increases the probability of sampling neutrons in important regions of phase space.
In complex geometries, with streaming, current VR methods may face limitations.
This work focuses on one of these challenges: Deep penetration (streaming) – Neutrons travel through small gaps without many interactions. NPS >>

## Slide 3
No bin limitations Works with ITER’s Monte Carlo codes
Compatible with other VR techniques
To improve Monte Carlo simulations, we propose a neural network-based source biasing method that prioritizes neutron sampling in the most important regions of phase space.
So, what do we really need from a good variance reduction tecnique?
High resolution in all variables: position, direction, and energy
Fully compatible with ITER’s Monte Carlo codes
Proposed Approach

## Slide 4
1. Monte Carlo simulation, we estimate physical quantities by averaging the contribution of many sampled particles. The problem is that in complex situations, most particles don’t contribute.
2. To improve this, we use Importance Sampling. We change how particles are sampled. Instead of choosing them randomly, we give more chance to particles that are likely to contribute.
3. Now, what’s the best way to choose which particles to sample? In theory, the best probability is proportional to the contribution:
4. The Figure of Merit (FoM) tells us if the method is efficient​
Source biasing with neural network
we need to find out which particles are most important.
we need to sample more from the particles that matter.
we use a neural network to learn an approximation
of f(x) from a previous simulation.
?

## Slide 5
Modification to the D1SUNED code
This version allows us to save data for each particle: position, direction, energy, and tally contribution
Using the modified D1SUNED code, we run a simulation with a uniform source
()
()
()
Methodology
Step 1: Initial Simulation
It tells us which particles are important

## Slide 6
Use that data to train a neural network. The network learns to guess the probability that a particle will contribute, based on its starting conditions. (Python)
(x,y,z,u,v,w,e)
Methodology
Step 2: Train the Neural Network
This gives us an idea of the unknown function f(x) — the contribution.

## Slide 7
Methodology
Step 3: We generate new particles, using the neural network to sample more from important regions.
We run a new simulation with the new particles. We focus on the important ones
new
(x,y,z,u,v,w,e)
Tally
Step 4: Run the Biased Simulation
We also correct the weights

## Slide 8
2. Training the neural network to predict the relevance of a particle (or phase space), expressed as a probability function.
3. Sampling the source according to this probability.
4. Run a new simulation.
Neutronic
response
new
(x,y,z,u,v,w,e)
(x,y,z,u,v,w,e)
N iteraciones
()
()
()
Tally
Tally
1. Get the information about the importance of the source particle phase space.

## Slide 9
Aplication to a reference problem
We validated our method using a benchmark inspired by ITER’s TCWS, where N-16 decay gammas are a key radiation source.
256 oriented pipes emit towards a steel wall with 9 apertures. The tally region, where photon flux is measured, is located from the steel shielding block.
Geometry created in SpaceClaim, converted to MCNP format using GEOUNED.
This benchmark provides a controlled yet realistic test case to evaluate the effectiveness of neural network-based source biasing

## Slide 10
Run a simulation with a uniform source, using the modified D1SUNED code
Initial particle simulation 1e10 nps
Less than 230,000 particles contributed to the tally. For each particle, we recorded
its position, direction, energy, and contribution value
4. Neural network learns to predict contribution from input data
 training dataset: 60% contributing / 40% non-contributing histories
5. New 10⁷ particles sampled with adjusted weights.
6. Finally, we used the new particles in a second MCNP simulation
Applying the Method
Simulation (nps) |  | Source bias (1e7)
MEAN | (2.7848±0.0010)×10−10 | (2.7840±0.0012)×10−10
FOM | 7.6 | 119
Analogue (1e10)
As expected, the tallies are statistically equivalent
The Figure of Merit (FOM) increased significantly

## Slide 11
We used a neural network to estimate the contribution of particles to the tally, based on position, direction, and energy. This gave us an approximation of the ideal sampling function.
 It works across all phase space variables
Using this estimated function, we biased the source to sample more particles from the most important regions of phase space.
This method works for realistic geometries and source conditions, such as the CDGS.
 Is fully compatible with MCNP workflows used in ITER
Conclusion

## Slide 12
Limitations and future work
The method is still in early development.
The neural network learns only from particles seen in the first simulation.
In difficult problems, it may see few contributing particles.
Other variance reduction methods may be needed.
More tests are needed to check how well it works in complex cases.

## Slide 13
Thank you for your attention. Any questions?
emartinez@ind.uned.es

## Slide 14
Estimating Physical Quantities in Monte Carlo
I → Quantity we want to estimate → Contribution function → Variables (position, direction, energy, etc.)
Monte Carlo estimation
N → Number of histories ​ → Sampled values
Reducing Variance with Importance Sampling
→ Probability density function (PDF) used for sampling
Optimal PDF to minimize variance
Using Neural Networks to Improve Sampling:
New Monte Carlo estimator
Measuring Efficiency – Figure of Merit (FOM) ​
→ Variance of the estimator T → Computational time
Source biasing with neural network
→ Neural network-generated probability