## Slide 1: IFMIF-DONES related activities at Lithuanian Energy Institute
Andrius Tidikas, Gediminas Stankūnas, Simona Breidokaitė, Benjaminas Togobicki, Dilmurod Tuymurodov
and WPENS contributors
Lithuanian Energy Institute

## Slide 2: Outline
Introduction to the Lithium loop cell
Simplified model
  Key assumptions of source term modelling
Detailed model
  Extended assessment

## Slide 3: Lithium Loop Source Term
High-intensity deuteron beam (125 mA, 40 MeV) interacts with lithium
Key reactions:
  7Li(d,2n)7Be & 6Li(d,n)7Be → Beryllium-7 (dominant radioisotope)
  Neutron activation of SS316L & EUROFER → Activated Corrosion Products (ACPs)
Key considerations:
  Dissolution
  Deposition
  Trapping and purification efficiency
Bernardi, D., et al. J Fusion Energ 41, 24 (2022)

## Slide 4: Model and Assumptions
Simplified Lithium loop model
Lithium Loop System Components:
  Cold Leg (CL): Outflow from heat exchanger
  Cold Trap (CT): Mesh filter for Be-7 and impurities
  Heat Exchanger (HX): Maintains lithium temperature and impurity removal
Key Assumptions:
  Be-7 uniformly dissolved in lithium at 3.26E-05 appm
  Flow regime 300°C in the cold leg, and a 2% flow rate
  Two corrosion models:
    Basic: 2 µm/year corrosion for all components
    Reduced: 0.4 µm/year for CL, HX, hot leg; 0.133 µm/year for quench tank
  Gamma spectra calculated at 0s, 1h, 1d, 1 week decay
Notes: "We modeled the lithium loop with three main components. A crucial assumption is that Be-7 is homogeneously dissolved in lithium, and corrosion rates vary in different models. These assumptions allow us to estimate the radiation impact over time."

## Slide 5: Gamma Spectra Analysis
FISPACT-2 code was utilized for the spectral and decay calculations
Gamma Spectra Breakdown:
  Be-7: Peak at 477.6 keV, dominates activity in cold trap
  ACPs:
    HX & CL: Co-58, Co-60, Mn-54, Fe-55…
    Cold trap: 3 orders of magnitude higher Be-7 activity
  Spectra divided into 18 energy groups (0–5 MeV)
Key difference:
  Reduced corrosion model shows ~5x lower cobalt levels

## Slide 6: Dose Rate Calculations
MCNP 6 Simulations:
  Biological dose rates using ANSI/ANS 6.1.1-1977 conversion
  2×10⁹ particle histories per run
  tally planes used for spatial dose mapping
Dose Rate Findings:
  General range: 1–100 mSv/h (LLC)
  Peak values near sources: Up to 10 Sv/h and more (Cold Trap)
  Cold Leg causes radiation streaming through the ceiling

## Slide 7: Effect of Corrosion Models & Cooling
Cooling for 1 week:
  Be-7 activity reduced by ~10%
  ACPs (Co-58, Mn-54, Fe-55) decrease by ~20%
Reduced Corrosion Model Effects:
  Minimal impact on dose rates
  Cobalt isotopes lower in lithium but remain significant
10-Year Radionuclide Trends:
  Co-60 dominates dose rates
  Fe-55 dominates activity
  No new significant radionuclides form during decay
  Differences in corrosion models:
    EUROFER vs. SS316L affects cobalt & chromium levels
    Cobalt moderately soluble → higher presence in basic model
    Chromium less soluble → minor impact

## Slide 8: Update on LLC
Lithium Dump Tanks (DT) & Electro-Magnetic Pumps (EMP)
Lithium Dump Tanks (DT) Functions:
  Store and melt lithium during system startup
  Collect lithium during shutdowns (normal or emergency)
  Purify lithium via nitrogen trapping
Updated Design: Two separate tanks
  DT1: Lithium storage and melting
  DT2: Lithium purification with nitrogen trapping
Electro-Magnetic Pumps (EMP):
  Ensure continuous lithium flow
  Provide redundancy for safety compliance
CAD to MCNP:
  McCAD was used in Salome environment.

## Slide 9: Shielding Considerations
Radiation Sources in Lithium System:
  Be-7
  ACPs
Shielding Approaches:
  DT shielding: 100 cm cover of standard concrete, 50 cm separation wall
Expected results:
  Room R016 dose rates: 1–100 mSv/h (up to 20 days after shutdown)
  Shielded DT reduces dose to μSv/h levels

## Slide 10: New modelling assumptions
Variance Reduction with ADVANTG:
  Improves accuracy near leakage points
  Reduces uncertainties by 10%
Assumptions:
  Beam off scenario (lithium in DT, traces in the pipes)
  Beam on scenario (lithium circulated in pipes, traces of lithium in DT)
  Standard vs. heavy concrete
Lithium traces were not considered!

## Slide 11: Dose Rate Calculations – Beam-Off Scenarios
Case 1: Ordinary Concrete Shielding (Beam-Off)
  DT pit with 1m concrete cover + 50cm separation wall
  Dose rate outside shielding: 10 μSv/h
Case 2: Heavy Concrete Shielding (Beam-Off)
  Same geometry
  Dose rate reduced to 1 μSv/h

## Slide 12: Dose Rate Calculations – Beam-On Scenario
Case 3: Beam-On with Lithium in Piping
  Dose rates: Up to 10⁴ μSv/h inside LLC room
External Exposure:
  Corridor C002: 10 μSv/h
  Cold Trap Cell (R009-1): 1 μSv/h
Shielding Effectiveness:
  1m of concrete shields most of LLC room
  Heavy concrete reduces external dose by 10x

## Slide 13: Summary
Key Findings:
  Reduced corrosion model has limited impact on dose reduction
  Beam-off dose rates are manageable with shielding
  Beam-on operation causes high radiation fields (10⁴ μSv/h)
  Heavy concrete is around 10 times greater in mitigating dose rates outside DT
  Radiation Levels in adjecets rooms
Things to consider
  ACP and Be-7 trapping optimization
  Improved shielding designs
  Refinement of corrosion models