## Slide 1
JSIR2S code system overview
Ylenia Kogovšek Žiber, ylenia.ziber@ijs.si
dr. Klemen Ambrožič, prof. dr. Luka Snoj, dr. Igor Lengar
Fusion Neutronics Meeting 2025, Madrid, 6.4. – 11.4.2025

## Slide 2: Introduction
Shutdown Dose Rate calculations ensure:
  Safe maintenance
  Safe decommissioning
  Protection of sensitive equipment
Two methods:
  R2S, Rigorous two-step
  D1S, Direct one-step
Most SDDR codes are proprietary and only validated for fusion applications

## Slide 3: Motivation
JSIR2S code (JSI) was evaluated based on measurements at the TRIGA research reactor
  Fission applications
  Fusion applications
Validation for both applications
Fusion applications:
K. Ambrožič, R. Villari, P. Batistoni, L. Snoj, Application of the JSIR2S code package for Shutdown dose rate calculations on JET, Proc. Int. Conf. PHYSOR2020 – Physics of Reactors: Transition to a Scalable Nuclear Future, 274, 2021
Fission applications:
K. Ambrožič, L. Snoj, JSIR2S code for delayed radiation simulations: Validation against measurements at the JSI TRIGA reactor, Progress in Nuclear Energy, Volume 129, 2020

## Slide 4: Computational methodology – JSIR2S Workflow
Workflow:
  Primary neutron radiation:
    Modified MCNP v6.2
  Secondary photon radiation:
    FISPACT-II handles isotopic activation and transmutation
    BetaShape calculates beta decay emission spectra.
    Photon transport with MCNP
Simulation Details:
  Mesh: 57.1 cm × 57.1 cm × 58 cm voxels
  Particle simulations:
    Neutron transport: 1×10⁹ particles using ENDF/B-VIII.0.
    Photon transport: 2×10⁹ particles via probability data sampling
    Isotope analysis: 5×10⁹ particles simulated
Reference: dr. Klemen Ambrožič
MCNP model
User defined irradiation scenario, mesh size, inventory libraries, isotopic return timestamps
Stohastic volume calculations and tally size determination
Neutron particle flux and spectra calculations
Isotopic inventory calculations
Decay particle transport

## Slide 5: Tokamak model
Simplified model of a large tokamak
  Diameter of 10 m and height of 6.5 m
3 different positions in 5 cm radius spheres:
Reference: prof. dr. Luka Snoj
Understanding and learning the workflow

## Slide 6: Tokamak model – materials
Materials:
  air,
  inconel,
  iron,
  copper,
  collemanite,
  steel,
  microthermal insulation,
  carbon and
  water.
Investigated isotopes:
  Cr50
  Fe54
  Fe58
  Ni58
  Cu63
  Cu65

## Slide 7: Irradiation scenario
DD plasma source similar to the one, present in the JET tokamak
volume averaged dose rate calculations
Simplified irradiation scenario similar to the JET irradiation scenario
  From the year 1988 until the year 2016
    Neutron yield of 1.5×1015 for 13 s
The ICRP-116 fluence to dose
conversion factors
Shutdown dose rate maps 12 days after shutdown

## Slide 8: Results -SDDR
T [days] | Cell A DR (μSv/h) | Cell A Rel. Unc. | Cell B DR (μSv/h) | Cell B Rel. Unc. | Cell C DR (μSv/h) | Cell C Rel. Unc.
12 | 4.87 | 0.09 | 3.44 | 0.11 | 0.74 | 0.22
30 | 3.76 | 0.08 | 2.56 | 0.11 | 0.79 | 0.20
60 | 3.26 | 0.08 | 2.12 | 0.10 | 0.51 | 0.21
120 | 1.88 | 0.08 | 1.32 | 0.09 | 0.18 | 0.25
SDDR over time,
up to 120 days
Locations A, B and C

## Slide 9: Results – Isotope analysis
Partial isotope analysis:
  Parent isotopes contributing the most to the SDDR (in Cell A)
At 2 hours after shutdown: Mn55, Cu63 and Cu65.
At 120 days after shutdown: Ni58.
Chart: 2 hours after shutdown
| Mn55 | Cu63 | Cu65 | Ni58 | Fe58 | Cr50 | Fe54 | Ba132 | Other
Sales | 0.4 | 0.05 | 0.02 | 0.0014932 | 5.1414e-05 | 1.6487e-05 | 5.3415e-06 | 9.2e-07 | 0.52
Chart: 12 days after shutdown
| Mn55 | Cu63 | Cu65 | Ni58 | Fe58 | Cr50 | Fe54 | Ba132 | Other
Sales | 9.343e-12 | 6.4444e-13 | 0.006 | 0.94 | 0.032 | 0.009 | 0.004 | 0.00060556 | 0.008

## Slide 10: Conclusion
In this study, the JSIR2S code was evaluated for SDDR calculations
A partial isotope analysis was performed to determine the dominant parent isotopes for the SDDR
Cu63, Cu65 and Mn55 contributed the most to the SDDR 2 hours after shutdown
Ni58, Fe58 and Cr50 contributed the most to the SDDR 120 days after shutdown
Future work:
  Validation with other codes
    Comparison of simulations

## Slide 11: Conclusion
Thank you for listening!
Any questions?